# FEATURES

- Meets ANSI/EIA/TIA 568-B.2-1 and ISO/IEC 11801 Standards

- New version 110D IDC type terminal blocks (use 110 or Krone type tool)

- Color-coded labeling for T568A and T568B wiring schemes

- 180° angle type (horizontal)

- 1000Base-T Copper Gigabit Ethernet ready

- Compatible with Cat. 3, 4, 5, 5e, and 6 cabling

- Works perfectly with TC-PDT Punch Down Tool

- Operating temperature: -40° ~ 80° C (-40° ~ 176° F)

- UL E157358 listed

- Standard 19” Rack-mount design

- 1-year warranty

TC-P16C6	16-Port Cat. 6 RJ-45 UTP Rack Mount Patch Panels

TC-P24C6	24-Port Cat. 6 RJ-45 UTP Rack Mount Patch Panels

TC-P48C6	48-Port Cat. 6 RJ-45 UTP Rack Mount Patch Panels

TC-1KC5EG	1,000 Feet Solid Cat. 5e UTP Cable

TC-RJ45E/100	 100 Count Cat. 5e RJ-45 UTP Connectors

TC-PDT	Punch Down Tool with 110 and Krone Blade

TC-NT2	Network Cable Tester (TP and Coax)

#### To order please call: 888-326-6061

#### 3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sates: sales@trendware.com • Support: Techsupport@trendware.com

Ss06272003

# Text boxes

TC-P16C6/TC-P24C6

TC-P48C6

PRODUCT

INFORMATION

### Cat. 6 16/24/48-Port Patch Panels

Prepare yourself for Copper Gigabit Ethernet with TRENDnet's Cat. 6 RJ-45 UTP Patch Panels. These patch panels are certified for 250Mhz Category 6, which are perfect for Copper Gigabit Ethernet connections. TRENDnet's 16/24/48-port Cat. 6 Patch Panels are ideal for Ethernet, Fast Ethernet and Copper Gigabit Ethernet (1000Base-T) network applications. Using TRENDnet's Cat. 6 products now, will prepare you for the high bandwidth network in the future without re-cabling your network.