Features

- Compliant with IEEE 802.3, IEEE 802.3μ, and IEEE 802.3x Standards

- Plug-and-Play (PnP) for auto-configuration

- Supports WOL for PCI Version 2.2

- Supports 32-bit PCI bus master specification Rev 2.1/2.2

- Supports Full-duplex mode that doubles the data rate up to 200Mbps

- Supports Full-duplex flow control (IEEE 802.3x)

- Supports 10/100Mbps N-way auto-negotiation

- Easy-to-view LED indicators

- Built-in FIFO buffers reduces overhead of memory transfers

- Compatible with Windows 95/98(SE)/ME/2000/XP/2003 Server

- Compliant with PC99 Standard

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T, IEEE 802.3μ 100Base-TX ANSI/IEEE 802.3 Auto-Negotiation IEEE 802.3x Full-Duplex Flow Control |
| Interface | 32-bit PCI BUS Rev 2.1/22 |
| Protocol | CSMA/CD |
| Network Media | Ethernet: UTP/STP CAT3, 4, 5 EIA/TIA-568 100-ohm screened twisted pair Fast Ethernet: UTP/STP CAT5, EIA/TIA-568 100-ohm screened twisted pair |
| Data Transfer Rate | 10Mbps: 10/20Mbps (Half/Full-duplex) 100Mbps: 100/200Mbps (Half/Full-duplex) |
| Diagnostic LED | Link, Activity |
| Network Drivers | Novell NetWare ODI, NDIS, SCO UNIX, LAN Manager Windows 95/98/2000/NT/XP/2003 Server Linux |
| Temperature | Operating: 0( C ~ 50( C (32( F ~ 122( F) Storage: -20( C ~ 70( C (-4( F ~ 158( F) |
| Humidity | Operating: 10 % to 90 % non-condensing Storage: 5 % to 90 % non-condensing |
| Certifications | FCC, CE |

TOP REASONS THE TE100-PCIWN IS A LASTING TREND

| Integration Friendly | Trouble free and easy installation |
| --- | --- |
| Economical | Compliant with PC99 standard and power saving mode, TRENDnet PCI Plug and Play Adapter is the perfect choice for cost-effective and high-bandwidth networking. |
| Flexible | Plug it in and ready to go |
| Performance | Operates in the 32-bit bus master mode, delivering throughputs as multi-megabits per second with little stress on the host’s CPU |

Package Contents	Related Product

- TE100-PCIWN	- TE100-PCIWA

- Multi-Language User’s Guide	- TE100-S5Pplus

- Driver Diskette	- TEG-PCITXR

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

TE100-PCIWN

10/100Mbps Fast Ethernet PCI Adapter

TRENDnet TE100-PCIWN is a 10/100Mbps Fast Ethernet Plug-and-Play PCI adapter. Utilizes the latest chipset technology and provides easy installation.  Automatic sense and connects to Fast Ethernet network with a RJ-45 connector. With TRENDnet adapter, your desktop will turn into a high-bandwidth graphic and multimedia workstation or a power server running at full-duplex speed.