Features

- 8 x 10/100Mbps Auto-MDIX Port

- 1 x 100Base-FX SC type Multi-Mode Fiber Port

- Supports switch Fabric up to 3.8GBps

- Layer 2 Management Switch with Full Software Support

- IGMP Snooping with Query Mode Support for Multi-Media Application

- Supports Broadcast Storm Filtering

- Supports Port Status Control (Status, Auto-Negotiation, Speed, Duplex and Flow Control)

- Supports Port Trunking with Flexible Load Distribution Control and Fail-Over Functions

- Supports Port-Based VLAN and IEEE 802.1Q Tag-Based VLAN

- Supports IP Multicast, Port Mirroring, Spanning Tree, SNMP and RMON

- Supports Port Security and IEEE 802.1p Class of Services

- Store-and-Forward Switching Architecture with Non-Blocking Wire-Speed Performance

- Configuration via RS-232 Console Port, Telnet, and Web Browser (HTTP)

- TFTP Firmware Upgrade via Browser

- Configuration File Save and Restore Feature Support

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T Ethernet; IEEE 802.3u 100Base-TX Fast Ethernet IEEE 802.3x Flow Control; IEEE 802.1D Spanning Tree IEEE 802.1q Tag-based VLAN; IEEE 802.1p Class of Service IEEE 802.3ad Link Aggregation |
| Interface | 8 x 10/100Mbps Auto-MDIX RJ45 Fast Ethernet Port 1 x 100Base-FX SC type Fiber Port |
| Packet Forwarding and Filtering Rate | 100M Ethernet: 148,800 packets per second per port 10M Ethernet: 14,880 packets per second per port |
| Cabling | Fast Ethernet: UTP/STP Cat. 5, EIA/TIA-568 100-ohm, 100 meters max Fiber: (50/125um, 62.5/125um), 2km max |
| Console Port | RS-232, female 9-Pin Serial Port (M-M serial cable included) |
| Protocol/Topology | (CSMA/CD) / Star |
| Buffer Memory | 2Mbits Data Buffer |
| Filtering Address Table | 8K MAC Address Entries |
| Bandwidth | Up to 3.8Gbps |
| LED Display | Power, Link/Activity, Full Duplex/Collision |
| Power | Input: 100~240VAC, 50/60Hz Internal Power Supply |
| Power Consumption | 17 watts |
| Dimensions | 250 x 133 x 37mm (9.8 x 5.2 x 1.5 inch) (W x H x D) |
| Weight | 1.08 Kg. (2.4 lb.) |
| Temperature | Operating: 0( ~ 45( C (32( ~ 113( F) Storage: -40( ~ 70( C (-40( ~ 158( F) |
| Humidity | 10% ~ 90% non-condensing |
| Safety Emissions | FCC, CE |
| Software |
| Management | Web Management, RS-232 Console Management, Telnet |
| Trunk | Max 4 Groups ( up to 4 Ports per group) |
| Class of Service | Supports High and Low Priority |
| QoS | Supports 8 Levels Priority and Mapping to High/Low Priority Queue for Class of Service |
| VLAN | Up to 256 VLAN groups and up to 4094 VLAN ID |
| IP Multicast | IGMP Snooping up to 256 groups 2 Types of Query Mode: Enable/Disable or Auto Query |
| Filter Database | Port Static MAC address lock, MAC filter and Port Security |
| Port Mirror | Up to 8 ports |
| Broadcast Control | None, 5%, 10%, 15%, 20%, 25% |
| Spanning Tree | IEEE 802.1d Support |
| RFC Standard | RFC1157 SNMP, RFC 1213 MIB II, Bridge MIB, RFC 1643 Ethernet Like, RFC 1493 Bridge MIB, RFC 1757 RMON1, RFC 1215 Trap, RFC 768 UDP, RFC 783 TFTP, RFC 791 IP, RFC 792 ICMP, RFC 854 TELNET Server/Client, RFC 1112 IGMP, RFC 2068 HTTP, private MIB, RFC 2674 VLAN MIB |

Packaging Contents			Related Products

- TE100-S800i			- TE100-S810Fi

- CD-ROM (User’s Guide)		- TEG-081Fi

- Quick Installation Guide

- RS-232 Cable / Power Cord

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

8-Port 10/100Mbps Layer 2 Managed Switch

with 100Base-FX Port

The 8-port 10/100Mbps Layer 2 Managed Switch provides exceptional performance, ease of use and flexibility for expanding business networks with fiber connection.  Utilizing a robust 3.8Gbps backplane, your managed switch can easily accommodate multiple switches and relieve server congestion by using its built-in fiber port. Advanced management features include SNMP, VLAN, IGMP, and Port security.

TE100-S810Fi

Management Switch Network Solution