Features

- 24 x 10/100/1000Mbps Auto-negotiation, Auto-MDIX Gigabit Ports

- Full/Half-Duplex Transfer Mode for Each Port (2000Mbps Full-Duplex only)

- Full Wire-Speed Non-Blocking Reception and Transmission

- Store and Forward Switching Method

- 512K bytes RAM Data Buffer and 8K entries MAC Address Table

- Extensive Diagnostic LED’s on the Front Panel

- IEEE 802.3x Flow Control for Full-Duplex Mode; Back Pressure Flow Control for Half-Duplex Mode

- Proprietary Windows Based Management/Monitoring Utility (similar to SNMP Trap)

- Port-Based VLAN and Port-Based IEEE 802.1p QoS (High/Normal)

- Supports Trunking (max. 3 groups/4ports each group) and Port Mirroring

- Port Setting Function, Users can set each Port’s Availability, Speed, Duplex Mode, and Flow Control

- Easy configuration via Web browser

- Standard 19” (1U) Rack Mount Size

- 5-Year Warranty

# Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3ab 1000Base-T IEEEE 802.3x Full Duplex Flow Control |
| Network Media | Ethernet: 2-pair UTP Cat. 3, 4, 5, up to 10Mbps Fast Ethernet: 2-pair UTP Cat. 5, up to 100Mbps Gigabit: 4-pair UTP Cat. 5, 5E, 6, up to 1000Mbps |
| Transmission Method | Store-and-Forward |
| Transfer Rate | Ethernet: 10Mbps/20Mbps (Half/Full Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full Duplex) Gigabit: 2000Mbps (Full Duplex) |
| Data RAM Buffer | 512Kbytes |
| Filtering Address Table | 8K entries per device |
| Switch Fabric | 48Gbps Forwarding Capacity |
| LED | Per Unit: Power Per Port: Link/ACT, 1000M, 100M |
| Power Supply | 100~240V AC, 50/60Hz, Internal Power Supply |
| Power Consumption | 35 watts. (max) |
| Dimension | 440 x 210 x 44 mm (17.3 x 8.27x 1.73 inch) |
| Weight | 3Kg (6.6 lb) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104(F) Storage: -10( ~ 70( C (14( ~ 158(F) |
| Humidity | 10% ~ 90% (non-condensing) |
| Emissions | FCC, CE |

Related Products					Package Contents

- TEG-224WSplus					- TEG-S240WS

- TEG-2248WS						- Multi-Language Quick Installation Guide

- TEG-448WS						- Rack Mount Kit

- TEG-160WS						- Power Supply

## To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Official Site: www.TRENDnet.com

# Text boxes

TEG-240WS (ver. B1.1R)

24-port 10/100/1000Mbps Gigabit

Web Smart Switch

TEG-240WS 24-port 10/100/1000Mbps Web Smart Switch is the ideal Switch for network segmenting.  It has 24 10/100/1000Mbps Auto-Sensing and Auto-MDIX ports for easy installation. TEG-240WS supports web browser configuration; Network Administrator can use web browser to configure port speed, port-based VLAN and QoS, and also monitor each port’s status which provides simple migration, scalability, and flexibility to handle new applications and data types. TEG-240WS is powerful and easy-to-use in reducing unnecessary broadcast traffic and enhance network security.