Features

- 48 x 10/100/1000Mbps Auto-Negotiation and Auto-MDIX Gigabit Ethernet UTP Ports

- 4 x 1000Mbps Auto-Sense mini-GBIC slots, Share with 4 1000Base-T Ports (Port 45-48)

- Full/Half-Duplex Transfer Mode for each Port

- Store and Forward Switching Architecture

- Integrated address Look-Up Engine with 8K absolute MAC address table

- Supports 1632K bytes RAM Data Buffering

- IEEE 802.3x Flow Control for Full/Half  Duplex Mode

- Back Pressure Flow Control for Half Duplex Mode

- Supports Tag VLAN, Qos , Trunking and Port Mirroring through Web-Based.

- Port Settings function, users can set each Port’s Availability, Speed, Duplex mode and Flow Control

- Easy Window Based Management Utility and Web-Based Configuration

- Extensive Diagnostic LED’s on the front panel

- Standard 19”  (1U) Rack-Mount Size (Kit included)

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3ab 1000Base-T IEEE 802.3z 1000Base-SX/LX (GBIC) IEEE 802.3x Full Duplex Flow Control |
| Network Media | Ethernet: UTP/STP Cat. 3, 4, 5 Fast Ethernet: UTP/STP Cat. 5 Gigabit: UTP/STP Cat. 5, 5E, 6 |
| Protocol /Topology | CSMA/CD, Star |
| LAN Ports | 48 x 10/100/1000Mbps Auto Negotiation Gigabit Ethernet ports 4 x Mini-GBIC slots, Share with 4 1000BASE-T Slots (Share with 4 1000Base-T Ports) |
| Data Transfer Rate | Ethernet: 10Mbps/20Mbps (Half-Duplex/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half-Duplex/Full-Duplex) Gigabit Ethernet: 2000Mbps (Full-Duplex) |
| Address Table | 8K Entries |
| Data RAM Buffer | 1632KBytes |
| Diagnostic LEDs | Per Unit: Power, System Per Gigabit Ethernet: Link/ACT Per Cooper Gigabit Port: Link/ACT, Speed (1000M-Green, 100M-Amber) Per Mini-GBIC Gigabit Port: Link/ACT |
| Power/Consumption | 100-240V AC, 50/60Hz Internal Power Supply / 70 Watts (Max) |
| Dimensions (W x D x H) | 440 x 310 x 44 mm (17.32" x 12.25" x 1.73") |
| Weight | 4.43kg (9.75 lbs) |
| Temperature | Operating : 0( C ~ 40( C (32( F ~ 104( F) Storage: -10( C ~ 70( C (14( F ~ 158( F) |
| Humidity | Operating: 10% ~ 90% RH Storage: 5% ~ 90% RH |
| Certifications | FCC Class A, CE Class A |

Package Content						Related Product

- TEG-448WS						- TEG-2224WS

- Quick Installation Guide					- TEG-2248WS

- Utility CD-ROM						- TEG-160WS

- Power Cord

- Rack-Mount Kit

## To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • TEL: (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

Front View

TEG-448WS

48-Port Gigabit Web-Based Smart Switch

TRENDnet’s TEG-448WS 48-Port 10/100/1000Mbps and 4-Slot Mini-GBIC Web-Based Smart Switch delivers high performance and scalability for large enterprises. Its Mini-GBIC slots can use either single or multimode fiber for constructing a high-speed network backbone. The 48-port Copper Gigabit ports support Auto-MDIX and Auto-Sensing for troublefree network integration. The TEG-448WS supports advanced network protocols such as VLAN, QoS, Trunking, and Mirroring.

Network Solution for TEG-448WS

Optional Module

- TEG-MGBSX

- TEG-MGBS10

- TEG-MGBS30

- TEG-MGBS50

- TEG-MGBS70