#### Mini-GBIC Features (TEG-MGBSX, TEG-MGBS10, TEW-MGBS40, TEW-MGBS80)

- Compliant with IEEE 802.3z Gigabit Ethernet and Fiber Channel Standards

- Industry standard SFP package

- Duplex LC connector

- 1.0625Gbps Fiber Channel Compliant

- 1.25Gbps Gigabit Ethernet Compliant

- Single 3.3V Power Supply Voltage

GBIC Features (TEG-GBSX, TEG-GBS10, TEG-GBS40, TEG-GBS80)

  - Compliant with Gigabit Interface Converter Specification SFF-8053, REV 5.5

  - Compliant with IEEE 802.3Z

  - SCA-2 Host Connector

  - Duplex SC connector

  - 3.3V and 5V Power Supply

  - Extended EMI & ESD Protection

  - Class 1 Laser product complies with EN 60825-1

#### Specifications

| Model Name | Wavelength | Media | Pout | Sensitivity | Power Budget | Distance |
| --- | --- | --- | --- | --- | --- | --- |
| TEG-MGBSX | 850nm | MMF | -9 ~ -3dBm | -18 | 9dBm | 550m |
| TEG-MGBS10 | 1310nm | SMF | -9 ~ -3dBm | -20 | 11dBm | 10km |
| TEG-MGBS40 | 1310nm | SMF | -3 ~ +2dBm | -23 | 20dBm | 40Km |
| TEG-MGBS80 | 1550nm | SMF | 0 ~ 5dBm | -23 | 23dBm | 80km |
| TEG-GBSX | 850nm | MMF | -9 ~ -3dBm | -18 | 9dBm | 550m |
| TEG-GBS10 | 1310nm | SMF | -9 ~ -3dBm | -20 | 11dBm | 10km |
| TEG-GBS40 | 1310nm | SMF | -3 ~ +2dBm | -23 | 20dBm | 40km |
| TEG-GBS80 | 1550nm | SMF | 0 ~ 5dBm | -23 | 23dBm | 80km |

MMF: Multi-Mode Fiber	SMF: Single Mode Fiber

#### Application

- Switch to Switch Interface

- High Speed I/O for File Server

- Distributed Multi-Processing

- 5-Year Warranty

# Text boxes

Mini-GBIC

1000Mbps-LX Mini-GBIC modules are designed to connect with any Gigabit Ethernet Switch with the industry standard GBIC slot.

GBIC

1000Mbps-LX GBIC modules are designed to connect with any Gigabit Ethernet Switch with a standard GBIC slot.