FEATURES

- IEEE 802.3, 802.3u and 802.3ab compliant

- Support 32/64-Bit PCI Local Bus Master high-speed operation of Rev. 2.2 specification

- One RJ-45 port with Auto Sensing and Auto MDI-X Medium Type Detection

- Supports Full-Duplex mode and doubles the bandwidth to 20/200/2000Mbps

- Supports Win98SE/ME/NT4/2000/XP, Linux and Netware

- 802.3 Full Duplex Flow Control, including Automatic Transmission of Pause Frames based on Rx FIFO thresholds

- 128KB RAM On-Chip Buffer

- Supports PCI 2.2 Wake-on-LAN for remote wake up

- Plug and Play Installation

- 5-Year Warranty

TREND SPEC’S

Standards: 			IEEE 802.3 10Base-T Ethernet

IEEE 802.3u 100Base-TX Fast Ethernet

IEEE 802.3ab 1000Base-T Gigabit Ethernet

ANSI/IEEE 802.3 Auto-Negotiation

Protocol:			CSMA/CD

Data Transfer Rate: 		Ethernet:  10Mbps/20Mbps (Half/Full Duplex)

Fast Ethernet: 100Mbps/200Mbps (Half/Full Duplex)

Gigabit Ethernet: 2000Mbps (Full-Duplex)

Cabling:			Ethernet: 2-pair UTP Cat. 3,4,5

Fast Ethernet: 2-pair UTP Cat. 5

Gigabit Ethernet: 4-pair UTP Cat 5/Cat 5E

Host Interface: 		32/64-bit PCI Rev.2.2

Connector:			Single RJ-45 UTP/STP, Auto MDI-X

Diagnostic LEDs:		Link: 10, 100,1000Mbps

ACT, FDX/COL

Power Consumption:	4.25 watts (max)

Driver Support:		Windows 98SE/ME/NT4/2000/XP,

Linux Kernel 2.4.13 or above,

Netware 5.x/6.x

Operating Temp.:		0( to 40( C (32( to 104(F)

Storage Temp.:		-10( to 70( C (14( to 158(F)

Operating Humidity:		10 % to 90 %

Storage Humidity:		5% ~ 90%

Certifications:		FCC Class B, CE Class B, VCCI Class B

TOP REASONS THE TEG-PCITXM2 IS A LASTING TREND

Performance: 	The full-duplex Gigabit adapter brings high bandwidth with up to 2000Mbps speeds.

User Friendliness:	Plug and Play with drivers support all popular network operating systems.

Flexibility:	Single RJ-45 connector auto detects 10/100/1000Mbps connection speed, Half/Full duplex mode, and Auto MDI-X medium type.

Cost-Effectiveness:	Provides the benefit of Gigabit Ethernet networking with the familiarity of Ethernet that operates in existing 64-bit PCI Bus.

TEG-PCITXM2	64-Bit 10/100/1000Mbps Copper Gigabit PCI Adapter

TEG-S18TXE	9-port 10/100/1000Mbps Copper Gigabit Switch

TE100-PCIWN	10/100Mbps Fast Ethernet PCI Adapter/Realtec Chipset

TE100-S55E+	5-port 10/100Mbps NWay Mini Switch

TE100-PS3+	10/100Mbps Multiple Protocol Direct Print Server (3 Parallel)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

TEG-PCITXM2

PRODUCT

INFORMATION

64-bit 10/100/1000Mbps

Copper Gigabit PCI Adapter

TRENDnet’s TEG-PCITXM2 64-bit 10/100/1000Mbps Copper Gigabit PCI Adapter is a high-bandwidth network adapter that auto-senses connection speed, half/full-duplex mode, and auto MDIX medium type. Network administrators can monitor performance remote with Wake-On-Lan. Save money and boost your network speed to 2000Mbps bandwidth with your existing Cat5 cables.TRENDnet’s TEG-PCITXM2 is ideal for high traffic Power Servers, Network Gaming and Video Conferencing Multi-Media Workstations.

Network Solution for

TEG-PCITXM2