Features

- Stackable up to 8 Switches* (requires Gigabit Module); provides up to 192 10/100Mbps connections

(* You can stack 16 Switches together. But, for better network performance, we suggest stacking no more than 8 Switches.)

- Manage all uplinked or Stacked Switches with one IP address from local LAN or Internet (requires valid public IP. If the Switch is behind a Firewall/Router, please open Port 80 and the Agent Control Port 28019 for the Switch’s IP)

- 24 10/100Mbps Auto-Negotiation and Auto-MDIX Fast Ethernet Ports

- 1 Gigabit Module Slot for optional module with Copper and/or Fiber Gigabit connections

- Full/Half-duplex transfer mode for each 10/100Mbps port (1000Mbps port supports only full-duplex mode)

- Store-and-forward switching architecture with non-blocking wire-speed performance

- IEEE 802.3x flow control for full-duplex and collision-based back pressure function for half-duplex operation

- Broadcast Storm Filtering and Head-of-Line blocking Prevention

- Port-Based VLAN (256 Groups), IEEE 802.1q Tag-Based VLAN (PVID 1~255) and IEEE 802.1D Spanning Tree (STP)

- IEEE 802.1v protocol-based VLAN classifications and IEEE 802.1x Authentication and Authorization

- Port-Trunking with flexible load distribution control and fail-over functions (7 trunk groups, max 4 ports per group)

- IP Multicast, IGMP Snooping (version 2), and RMON Group 1,2,3,9

- 2-level priority queuing, Ingress port security mode and by-port Egress/Ingress rate control

- Configuration via Console Port (serial cable included), SNMP (v1.0, MIB II), TELNET, and Web Browser

- Upgradeable firmware via TFTP and Ping function from the Switch for network diagnostic

- Standard 19” Rack-Mount Size (rack-mount kit included)

- 5-Year Warranty

Specifications

| Standards | IEEE 802.3 10Base-T Ethernet IEEE 802.3u 100Base-TX Fast Ethernet IEEE 802.3z 1000Base-SX/LX Gigabit Ethernet IEEE 802.3x Flow Control IEEE 802.1D Spanning Tree IEEE 802.1q Tag-based VLAN, Priority Control IEEE 802.1v Protocol-Based VLAN IEEE 802.1x RADIU Authentication and Authorization |
| --- | --- |
| Interfaces | 24 x 100Base-TX RJ-45 STP Ethernet Ports 2 x 1000Base-TX RJ-45 Connector Ports or optional 1000Base-SX and/or 1 x RS-232 Serial Port |
| Packet Forwarding and Filtering Rate | 1000M Ethernet: 1,488,100 packets per second per port 100M Ethernet: 148,810 packets per second per port 10M Ethernet: 14,880 packets per second per port |
| Cabling | Fast Ethernet: UTP/STP Cat. 5, EIA/TIA-568 100-ohm, 100 meters max. 62.5/125um Multimode Fiber with SC-type connector, 2Km max. Gigabit Ethernet: UTP/STP Cat. 5, EIA/TIA-568 100-ohm, 100 meters max. 62.5/125μm Multimode Fiber with SC-type connector, 220 meters max. 50/125μm Multimode Fiber with SC-type connector, 550 meters max. |
| Console Port | RS-232, female 9-Pin Serial Port (serial cable included) |
| Protocol/Topology | (CSMA/CD) / Star |
| Buffer Memory | 1MB for Control, 3MB for Packet Filter |
| Filtering Address Table | 6K MAC (255 entry of Static MAC), 4K VLAN and 2K Multicast Entries |
| LED Display | Per Device: Power, Diagnostic, FAN1, FAN2. Per Port: Link, Activity, |
| Power Consumption | 30 Watts max. (Input: 100~240VAC, 50/60Hz Internal Power Supply) |
| Dimensions | 440 x 184 x 44mm (17.3 x 7.3 x 1.8 inch) (W x H x D) |
| Weight | 2.3 Kg. (5.1 lb.) |
| Operating Temperature | 5( ~ 45( C (41( ~ 113( F). Storage Temperature: -20( ~ 70( C (-4( ~ 158( F) |
| Humidity | Operating: 10% ~ 90% non-condensing |
| Certifications/Safety | FCC, CE/ CB, UL |

TOP REASONS THE TEG-S2500i IS A LASTING TREND

| Performance | Gigabit bandwidth between Stacking Switches and backbone. |
| --- | --- |
| Flexibility | Stack Switches in the same room or in different rooms. Single IP Management allows Administrator to manage/monitor all the Switches locally or remotely (requires public IP) using one IP address. |
| Expandability | Expand the network by connecting multiple Stacks of Switches together via Gigabit backbone. |
| Cost Effective | Provides SNMP management and Gigabit Performance at an affordable price. |
| Security | Administrator can setup 802.1Q or Port-based VLAN to further segmenting the network. |

| Optional Modules |
| --- |
| TEG-S24M2C | 2-Port 10/100/1000 Copper Gigabit Module |
| TEG-S24M1F | 1-Port Multimode SC-type Fiber Gigabit Module |
| TEG-S24M2F | 2-Port Multimode SC-type Fiber Gigabit Module |
| TEG-S24M100F | 1-Port Multimode SC-type 100Base-FX Module |
| TEG-S24M200F | 2-Port Multimode SC-type 100Base-FX Module |
| TEG-S24M11GF | 1-Port 10/100/1000Mbps Copper Gigabit + 1-Port 1000Base-SX/LX GBIC Multimode SC type Module |
| (Note: when stacking the Switches together, please install 2-Port module on all Switches, except the first and the last Switches. |

TEG-S2500i	24-Port 10/100Mbps Stackable SNMP Switch with Gigabit Slot

TEG-S2400i	24-Port 10/100Mbps SNMP Switch with Gigabit Slot

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

24-Port 10/100Mbps Stackable SNMP Switch

The TEG-S2500i 24 Port 10/100 Stackable SNMP Switch provides small and medium businesses with the foundation for a highly scalable and easily managed network. The Web/SNMP Managed Switch allows network administrators to remotely monitor and manage network performance and security. Network administrators can stack up to 8 Switches and manage them with only one IP address using a standard web browser. Server bottlenecks are a thing of the past with the Gigabit module slot that supports a series of optional Gigabit Copper, Gigabit Fiber and GBIC modules. Security and performance are optimized with advanced Port/Tag-based VLAN, QoS, Trunking and monitoring features.

TEG-S2500i

## Network Solution for TEG-S2500i

Product Information