FEATURES

- Operates as Access Point or WDS Wireless Bridge/Repeater mode

- Provides 64/128-bit Wired Equivalent Privacy (WEP) encryption and WPA Support

- Supports most operating systems, such as Windows 95/98/ME/NT/2000/XP, Unix and Mac

- MAC Address Control for Authorization Access (20 entries)

- Allow Users to disable ESSID Broadcast to increase wireless security

- 10/100Mbps Auto-Sensing Fast Ethernet Port

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps

- Allow auto fallback data rate for optimized reliability, throughput and transmission range

- Dual 2dBi Detachable Diversity Antennas. Replace with optional High-Gain antenna to extend the range/coverage area.

- Easy configuration and management with Web Browser

- Flash memory for Firmware Upgrade

- Distance coverage 40 to100 meters indoor, 100 to 300 meters outdoors depending on the environment

- 3-Year Warranty

TREND SPEC’S

Standards: 		IEEE 802.11b, 802.3u

Modulation Technology:	Direct Sequence Spread Spectrum (DSSS)

Channel:	11 Channel

Data Rate:	11Mbps, 5.5Mbps, 2Mbps, and 1Mbps (auto-fallback)

Operating Mode:	AP, Bridging, Repeater and AP Client

Frequency Range:	2.4 ~ 2.497 GHz

Security:	64/128-bit WEP Encryption, WPA

Antenna:	2 x 2dBi Detachable Diversity Antennas with Female Reverse SMA connector

Output Power:	13 dBm (min)

Transmit Power:	Adjustable 10dBm(12.5%), 12dBm(25%), 15dBm(50%) and 17dBm(100%)

Receiving Sensitivity:	11Mbps: -84dBm @ 8% PER (Packet Error Rate)

2 Mbps: -90dBm @ 8% PER (Packet Error Rate)

Media Connector:	10/100Mbps, Half/Full Duplex

LED Indicators:	Power, LAN & WLAN

Power:	5V, 2.4A External Power Adapter

Dimensions:	140 x 98 x 30 mm (5.5 x 3.85 x 1.2 inches) (without antenna)

Weight:	163 g. (5.76 Oz.)

Temperature:	Operating: -0( ~ 40(C (32( ~104(F); Storage: -10( ~ 70(C (14( ~ 158(F)

Humidity:	Max. 90% (non-condensing)

Certification: 	CE, FCC

TOP REASONS THE TEW-230APB IS A LASTING TREND

Integration Friendly: Supports both Ethernet and Fast Ethernet, with Web Browser

configuration for fast and easy setup.

Economical: Attaches to Ethernet network at anytime to add wireless users on the network. Save time, labor, and material for network cable installation.

Flexible: Works as stand-alone Access Point, Single/Multiple Access Point(s) Bridge, or Ethernet Access Point Client.

Security: Provides 64/128-bit WEP Encryption and WPA

Cost Effective:	 One unit provides multiple wireless connections to wired LAN.

TEW-230APB	802.11b 11Mbps Wireless Access Point

TEW-226PC	802.11b 11Mbps Wireless CardBus PC Card

TEW-228PI	802.11b 11Mbps Wireless PCI Adapter

##### To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

802.11b 11Mbps Wireless Access Point

TRENDnet’s TEW-230APB Wireless Access Point is today’s link to Wireless Technology.  Compliant with the IEEE Wireless Networking Standard 802.11b, it provides Direct Sequence Spread Spectrum (DSSS) operation for transparent bridging and roaming capabilities for wireless nodes. The TEW-230APB also provides WDS bridging functions, allowing users to connect two or more Access Points together, wirelessly.  With TRENDnet’s Wireless Access Point and Wireless Network Adapters, users can connect to Ethernet/Fast Ethernet LAN at home or office to access network resources such as hard drives, CD-ROM/DVD drives, network printers, and Internet connection - with coverage up to 300 meters.

TEW-230APB

Product Information

Wireless Solution for TEW-230APB