FEATURES

- Uses 2.4 GHz frequency band, which complies with worldwide requirements

- 32-bit PCI Bus Specification 2.2

- Up to 54Mbps connection speed

- Connects to IEEE 802.11g or 802.11b (11Mbps) wireless devices

- Dynamically shifts network speed (based on signal strength)

- Supports Ad-Hoc (peer-to-peer) mode and Infrastructure mode (Access Point)

- Compatible with Windows 98SE/ME/2000/XP

- 64/128-bit Wired Equivalent Privacy (WEP) with ASCII, HEX, or Passphrase Key

- Stores multiple Wireless Network Profiles

- Low interference and high susceptibility guarantee reliable performance

- Enables high data rate multi-media applications such as video streaming transmission

- 2dBi Detachable antenna with female Reverse SMA connector

- Distance coverage 30 to100 meters indoor, 100 to 300 meters outdoors

- 3-Year Warranty

TREND SPEC’S

Interface Type:		PCI Bus Power Management Specification 2.2

Standards:		IEEE 802.11b and IEEE 802.11g draft

Antenna:		2dBi Dipole Antenna with Reverse SMA connector

Data Rate (auto fallback):		802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps

802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps

Module Technique:		802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps)

802.11g: OFDM

Media Access Protocol:		CSMA/CA with ACK

Frequency:		2.4 to 2.497 GHz (Industrial Scientific Medical Band)

LED Indicator:		ACT (Activity)

Output Power:		15dBm (typical)

Receiving Sensitivity:			11Mbps 10 – 5 BER @ -80 dBm (typical)

54Mbps 10 – 5 BER @ -65 dBm (typical)

Channels:		11 Channels (US/Canada), 13 Channels (EU)

Power Consumption:			operating mode: 3.3VDC (TX: 550mA, RX: 350mA)

Sleep mode: 3.3VDC (TX: 225mA, RX: (disabled) <10mA)

Dimensions (LxWxH):		120 x 85 x 13 mm (4.7x 3.3 x 0.5 inches) (without the metal bracket)

Weight:		130g (4.5 oz.) with antenna

Operating Temperature:		0( ~ 50( C (32( ~ 122( F)

Storage Temperature:		-20( ~ 65( C (-4( ~ 149( F)

Humidity:	95% max. (Non-condensing)

Certification:	FCC, CE

##### TOP REASONS THE TEW-403PI IS A LASTING TREND

Economical:	Save time, labor, and materials; compare with wired network installation.

Flexible:	Creates wireless peer-to-peer network in Ad-Hoc mode or connects to Ethernet LAN in Infrastructure mode using Wireless Access Point or Wireless Router.

Cost Effective:	Supports IEEE 802.11b and IEEE 802.11g draft standards; connects to any IEEE 802.11b and 802.11g wireless network.

Performance:	54Mbps high-speed wireless connection.

TEW-403PI	54Mbps Wireless PCI Network Adapter

TEW-401PC	54Mbps 802.11g Wireless PC Card

TEW-410APB	54Mbps Wireless Access Point + Bridge

TEW-411BRP	54Mbps Wireless Broadband Router + Access Point

TEW-PS3	3-port Wireless Ethernet Print Server

TEW-PS1U	11Mbps Wireless USB port Multi-Protocol Print Server

TEW-IA04O	4dBi Omni Antenna (indoor) for IEEE 802.11b 2.4GHz ISM Band

TEW-IA06D	6dBi Directional Antenna (indoor) for IEEE 802.11b 2.4GHz ISM Band

TEW-OA14DK	14dBi Directional Antenna (outdoor) for IEEE 802.11b 2.4 GHz ISM Band with Mounting Hardware and 2 Meters Antenna Cable (TEW-2000F; Female N-Type and Female Reverse SMA Connectors)

TEW-OA24D	24dBi Directional Parabolic Antenna for 2.4GHz ISM Band with female N-Type connector

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com	SS06222003

# Text boxes

### 54Mbps 802.11g Wireless PCI Adapter

TRENDnet's TEW-403PI 54Mbps Wireless LAN PCI Adapter creates freedom for your desktop PC.  This PCI adapter plugs right into computer's PCI bus slot providing wire-free access to networked resources from your wired Local Area Network (LAN) and Internet (via Access Point) or create a network without networking cables.  It dynamically shifts between 54 and 1 Mbps for maximum availability and reliability.  Complying with 2.4 GHz frequency band IEEE 802.11g draft and 802.11b 11Mbps standards, TRENDnet's TEW-403PI ensures optimal security and performance for your wireless networking environment.

#### TEW-403PI

IEEE 802.11b/11g Wireless Network Solution

Product Information