Features

- Wi-Fi Compliant with IEEE 802.11a, 802.11g and IEEE 802.11b Standards

- Uses 5 GHz or 2.4 GHz Dual Band Design, which Complies with Worldwide Requirements

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure (AP-Client) Mode

- Supports Super AG technology Data Rate up to 108Mbps

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11a/g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Compatible with Windows 2000/XP (SP1/SP2)/2003 Server

- Supports 64/128-bit WEP, WPA (AES/TKIP)

- Supports Wireless Multimedia Enhancements Quality of Service (QoS IEEE 802.11e draft)

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Range of up to 100 meters indoors, 250 meters outdoors (depends on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | 32-Bit 3.3V CardBus Type II Card |
| Standards | IEEE 802.11a, IEEE 802.11b and IEEE 802.11g |
| LED Indicator | Power, Link |
| Power Consumption | Receive Mode: 230mA(max) ; Transmit Mode: 410 mA(max) |
| Supported OS | Windows 2000/XP (SP1/SP2), 2003 Server |
| Dimensions (LxWxH) | 115 x 54 x 4mm (4.5 x 2.1 x 0.16 inches) |
| Weight | 40g (1.3oz) |
| Temperature | Operating: 0( ~ 55( C (32( ~ 131( F) Storage: -20( ~ 85( C (-4( ~ 185( F) |
| Humidity | 10% ~ 90%max (Non-condensing) |
| Certification | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11a/g: OFDM with BPSK, QPSK and 16/64-QAM Sub-Carrier Modulations |
| Antenna | Built-in (1.5dBi ; 11b/g: 1dBi) Dual Band Antenna |
| Frequency | 802.11a: UNI-Band 5.15 ~ 5.825 GHz ; 802.11b/g: ISM-Band 2.400 ~ 2.4835 GHz |
| Media Access Protocol | CSMA/CA |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11a/g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps Super AG : 108Mbps |
| Transmit Power | 802.11a: 15dBm (typical) 802.11b: 19dBm (typical) 802.11g: 16dBm (typical) |
| Receiving Sensitivity | 802.11a: 54Mbps 10 – 5 BER @ -70 ±2 dBm (typical) 802.11b: 11Mbps 10 – 5 BER @ -88 dBm (typical) 802.11g: 54Mbps 10 – 5 BER @ -70 ±2 dBm (typical) |
| Encryption | 64/128-bit WEP, WPA |
| Channels | 11a: Subject to Local Regulations 11b/g: 1~11 (US), 1~13 (EU) |

##### TOP REASONS THE TEW-501PC IS A LASTING TREND

| Economical | Save Time, Labor, and Materials; Compare with Wired Network Installation |
| --- | --- |
| Flexible | Creates wireless peer-to-peer network in Ad-Hoc mode or connects to Ethernet LAN in Infrastructure mode using Wireless Access Point or Wireless Router |
| Cost Effective | Supports IEEE 802.11a, IEEE 802.11b and IEEE 802.11g Standards; Connects to any IEEE 802.11a and 802.11b/g wireless network |
| Performance | 108Mbps High Speed Wireless Connection |

Related Products		Package Contents

- TEW-503PI			- TEW-501PC

- TEW-504UB			- Utility & Driver CD-ROM

- TEW-510APB			- Multi-Language Quick Installation Guide

- TEW-511BRP

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

Official Site: www.TRENDNET.com

# Text boxes

### 108Mbps 802.11a/g Wireless CardBus PC Card

TRENDnet’s TEW-501PC 802.11a/g Wireless PC card is a flexible and affordable wireless solution that allows your mobile workstation to connect to three wireless networks:  802.11a, 802.11b, or 802.11g.  The TEW-501PC can operate at a blazing 108Mbps.  For wireless security, the TEW-501PC uses WPA-PSK with AES and TKIP encryption algorithms and WEP.

*Due to European Wireless Regulations, Super A mode is not supported in the EU version

#### TEW-501PC

Wireless Network Solution for TEW-501PC