Features

- Wi-Fi Compliant with IEEE 802.11n (draft) Standard

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Standards

- Supports Ad-Hoc(Peer to Peer) or Infrastructure (AP-Client) Mode

- High-Speed up to 300Mbps Data Rate using IEEE 802.11n connection

- Supports MIMO technology with Built-in 3 Internal Printed Antennas

- Dynamic Data Rate Scaling from 300Mbps to 1Mbps

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Universal Wireless Connectivity for Seamless Roaming among 802.11b/g/n Networks

- Supports 64/128-bit WEP, WPA/WPA2 and WPA-PSK/WPA2-PSK

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Compatible with Windows 2000/XP/Vista Operating Systems

- Easy User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | USB 2.0, 1.1 Standard |
| Standards | IEEE 802.11b, IEEE 802.11g and IEEE 802.11n (draft) 1.0 |
| Power Consumption | Receive Mode: 260mA(max) ; Transmit Mode: 420mA(max) |
| Supported OS | Windows 2000/XP/Vista |
| Dimensions (LxWxH) | 80 x 27 x 12mm (3.1 x 1 x 0.5 inches) |
| Weight | 20g (0.7oz) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104( F) Storage: -10( ~ 70( C (14( ~ 158( F) |
| Humidity | 10% ~ 95%max (Non-condensing) |
| Certification | CE, FCC |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM with BPSK, QPSK and 16/64-QAM sub-Carrier modulations 801.11n: OFDM, 64-QAM |
| Antenna | Built-in 3 Internal Printed Antennas |
| Frequency | 2.412 ~ 2.484 GHz |
| Media Access Protocol | CSMA/CA with AC |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps 802.11n (draft): up to 300Mbps |
| Output Power | 802.11b: 17dBm (typical) 802.11g: 14dBm (typical) 802.11n (draft): 13dBm (typical) |
| Receiving Sensitivity | 802.11b: -88dBm (typical) @ 10% PER 802.11g: -74dBm (typical) @ 10% PER 802.11n (draft): -66dBm (typical) @ 8% PER |
| Encryption | 64/128-bit WEP (Hex & ASCII), WPA/WPA2, WPA-PSK/WPA2-PSK |
| Channels | 1~11 (US), 1~13 (EU) |

Package Contents								Related Products

- TEW-624UB									- TEW-621PC

- Utility & Driver CD-ROM							- TEW-623PI

- Multi-Language Quick Installation Guide					- TEW-630APB

- TEW-631BRP

To order please call: 888-326-6061

20675 Manhattan Place, Torrance CA 90501 • (310) 961-5500 • Fax: (310) 961-5511

## Sales: sales@trendnet.com  • Support: support@trendnet.com

Tech Support Hotline: (866)845-3673

Official Site: www.trendnet.com

# Text boxes

### 300Mbps Wireless N USB 2.0 Adapter

The 300Mbps Wireless N USB 2.0 Adapter allows you to connect wirelessly with supercharged speed, range and reliability. Wireless speeds increase up to 300Mbps when connecting to TRENDnet Wireless N access points or wireless routers. This 802.11n device seamlessly connects to your wireless network without performance degradation.

#### TEW-624UB (H/W:V1.0R)