Features

- Compliant with 5GHz 802.11a and 2.4GHz 802.11b/g wireless devices with RP-TCN male

Connectors

  - Adapts RP-TNC connectors for use with TRENDnet RP-SMA antennas, cables and accessories

  - Optimized for use with TRENDnet’s Indoor/Outdoor antennas, antenna cables and surge protection kit*

- No configuration or installation software required.

- 3-Year Warranty

* Additional accessories might be required.

Specifications

| Electrical | Mechanical |  |
| --- | --- | --- |
| Impedance | 50 ohm Pin Configuration | RP-TNC Mating | 7/16-28 UNEF-2B Threaded Coupling |
| Frequency Range | DC ~ 6GHz | RP-SMA Mating | 1/4-36 UNS-2A Threaded Coupling |
| Voltage Rating | 500 Volts Peak | Mating Torque | 15 inch pounds (170 N.cm) max |
| Insertion Loss | 0.2dB Max | Connector |  |  |
| Dielectric Withstanding Voltage | 1000 Volts RMS | RP-TNC | Outer Connector: Inner Thread Inner Conductor: Female |
| Material |  | RP-SMA | Outer Connector: Outer Thread Inner Conductor: Male Pin |
| Body | Nickel Plated Brass |  |  |
| Contact | Gold Plated Berylium Copper | Environment |
|  |  | Temperature | -55 ºC ~ 85 ºC (-67 ºF ~ 185 ºF) |
| Insulator | Teflon | RoHS Compliant | Yes |
| Gasket | Rubber |  |  |

Packaging Contents

- TEW-ASAK

- Multi-Language Quick Installation Guide

To order please call: 888-326-6061

Sales: sales@trendnet.com

Support: support@trendnet.com

Tech Support Hot Line: 866-845-3673

www.trendnet.com

# Text boxes

Network Solution for TEW-AMBA

RP-TNC to RP-SMA Adapter

The RP-TNC to RP-SMA adapter is designed to connect an external antenna with a RP-SMA female connector to any 2.4GHz 802.11b/g and 5.8 GHz 802.11a wireless device. It is easy to install and no configuration or software is required. This device opens the door to variety of TRENDnet Antenna solutions.

TEW-AMBA (V1.0R)