Features

- Compatible with 2.4GHz 802.11b/g wireless devices

- Weatherproof housing suitable for outdoor applications

- Adjustable mount for optional orientation and performance

- Ideal for point-to-point bridge connections between buildings/zones

- Delivers extended access point range in expansive single floor environments

- Higher power output extends transmission range through low dB loss materials (plywood/plasterboard) used in typical floor and wall construction*

- Enhances wireless range and improves signal transmission and reception

- Boosts standard antenna power from meager 2dBi to a respectable 14dBi

- Easy-to-install wall and pole mounting

- 3-Year Warranty

* Due to the bisymmetrical nature of WiFi, the client segment may also require a high gain antenna.

Specifications

| Hardware |  |  |  |
| --- | --- | --- | --- |
| Frequency range | 2.4 ~ 2.5GHz | Connector | N-Type Female |
| Antenna Gain | 14dBi | Survival Wind Speed | 216 km/ hr (134miles/hr) |
| VSWR | 1.5:1 Max | Lightning protection | DC ground |
| Polarization | Linear, Vertical | Radome Material | ABS |
| HPBW/ Horizontal | 30° | Dimension | 225 x 228 x 30mm (8.9 x 9.0 x 1.2in.) |
| HPBW/ Vertical | 30° |  |  |
| Front to Back Ratio | 15dB | Weight | 450g (15.9oz.) |
| Power Handling | 50W (cw) | Temperature | -40oC ~ 80oC (-40oF ~ 176oF) |
| Impedance | 50 Ohms |  |  |

* Note: For optimal results in extending your wireless range with wireless antenna installations, we recommend that you consult a professional installer for site survey, safety precautions, and proper installation.

New Implement New Color Housing

Package Contents							Related Products

- TEW-AO14D							- TEW-AO08O

- Multi-Language Quick Installation Guide				- TEW-AO10O

- Mounting Guide							- TEW-AO19D

- Mounting Bracket							- TEW-L406/TEW-L412

- TEW-ASAK

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Technical Support: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

TEW-AO14D (Version 2.0R)

R

14 dBi Outdoor High-Gain Directional Antenna

TEW-AO14D Outdoor Directional Antenna provides long distance point-to-point connectivity for your wireless network. As an optional antenna for your IEEE 802.11b/g 2.4GHz wireless network equipment, you can install it outdoor for long distance point to point connections, or install it in a building to blast through obstructions. Enjoy the benefits of wireless connectivity at greater distances and throughput throughout your   outdoor wireless zone.

* This dBi gain does not factor cable loss. Performance estimations are for typical use; range will vary with site conditions.