Features

- Supports dual band 2.4GHz 802.11b/g and 5GHz 802.11a wireless devices.

- Multi-strike capability and bi-directional protection helps protect devices from the erratic and unpredictable nature of lightning

- Equipped with Cable Converter for flexible connection between rigid outdoor cable and Access Point

- Color coded cable and adapter sleeves ensures easy installation

- Easy-to-Install wall mounting

- No configuration or installation software required

- 3-Year Warranty

Specifications

| Surge Arrestor |  | Cable Convertor |
| --- | --- | --- |
| Electrical Specifications | Electrical Specifications |
| Frequency Range | DC ~ 6GHz | Tensile Strength | 11Kg |
| Tensile Strength | 50Kg | Impedance | 50 + 2.0Ω |
| VSWR | 1.2: 1 max ( DC ~ 4GHz ) 1.5: 1 max ( 4GHz ~ 6GHz ) | Conductor Resistance | 55.8 Ω/Km 20°C |
| Insertion Loss | 0.8dB max ( 0 ~ 6GHz ) | Insulator Resistance | 1000 MΩ/Km min. |
| DC Breakdown Voltage | 90V + 20% | Rating Temp Voltage | 80°C 30V |
| Impulse Discharge Voltage | 5KA min (wave 8/20 μs) 10KV min (wave 1.2/50 μs) | Spark Test | 2 KV |
| Impedance | 50Ω | Dielectric Strength | AC 1 KV/min |
| Insulation Resistance | DC 50V > 10000MΩ | Attenuation |
|  |  | 800 MHz | 0.8 dB/m |
| Mechanical Specifications | 1500 MHz | 1.0 dB/m |
| Connector Interface | N-Type Male to N-Type Female | 2000 MHz | 1.2 dB/m |
| Body Material | Copper | 2500 MHz | 1.25 dB/m |
| Temperature | - 20°C ~ 70°C (-4°F ~158°F) | 5800 MHz | 2.40 dB/m |
| Dimensions | 68 x 27 x 23mm (2.5 x 1.1 x 0.9in.) | Mechanical Specifications |
| Weight | 184g (6.5 oz.) | Connector Type | Reverse SMA Female to N-Type Male |
| Grounding Wire Cable Specification | Center Conductor | Tinned Copper |
| Grounding Wire Cable | 18 AWG | Dielectric Material | Foam Polyethylene |
| Rating Voltage | 600V | Shielded Material | Plain Copper Braid |
| Rating Temperature | 105°C (221°F) | Jacket Material | PVC |
| Conductor Resistance | 6.64 MΩ/KFT 20°C | Temperature | - 20°C ~ 70°C (-4°F ~158°F) |
| Insulation Resistance | 2.5 MΩ/KFT 20°C, in water | Length | 300mm (11.81 in.) |
| Voltage Withstand Test | 2 KV/min, in water | Weight | 51g (1.8 oz.) |

Detail View

Package Contents							Related Products

- TEW-ASAK	 (Surge Arrestor + Convertor)				- TEW-AO08O/ TEW-AO10O

- User’s Guide							- TEW-L202/TEW-L208

- Mounting Bracket 							- TEW-L406/TEW-L412

- Weatherproof Tape

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: support@trendnet.com • Tech Support Hotline: 1-888-777-1550

Official Site: www.trendnet.com

# Text boxes

N-Type Female
Connector

TEW-ASAK

Outdoor Arrestor Kit

The Outdoor Arrestor Kit provides lightning protection for your wireless equipment. By adding a simple arrestor to your wireless antenna, you can reduce the costs in damaged switches, access points, or other network devices.  Simply connect the Outdoor Arrestor Kit directly inline between your Access Point and your outdoor antenna cable, and connect the ground wire to a ground pole.

Reverse SMA 
Female Connector

Surge Arrestor

N-Type Male
Connector

Cable Convertor

Outdoor Arrestor Solution

Grounding Wire

Cable

N-Type Male
Connector

Antenna Solution with TEW-OA10O