Features

- Wi-Fi Compliant with IEEE 802.11b/g devices

- One RJ-45 10/100Mbps Auto-MDIX Fast Ethernet port

- IEEE 1284 male centronics (DB-36) parallel printer port

- Supports 64/128-Bit WEP & WPA-PSK encryption

- Compliant with Windows 98SE/2000/XP/2003 Server and more

- LPP Printing for Windows

- IPP Printing for Windows 2000/XP

- Printing over Email

- Second HTTP port for remote Web configuration and IPP printing

- Supports Macintosh Rendezvous Zero Configuration function

- Windows-Based program (PS Utility)

- Web-Based (HTTP) configuration

- Built-in flash memory for easy firmware upgrade

- 3-Year Warranty

*Mac Systems are only compatible with Post-Script printers

Specifications

| Hardware |
| --- |
| Standards | Wired: IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX Wireless IEEE 802.11b/g |
| Printer Interface | IEEE 1284 Male Centronics (DB-36) |
| LAN Port | 10/100Mbps Auto-Negotiation UTP/STP RJ-45 Port |
| CPU/ SDRAM / Flash ROM | RDC 2880 / 8Mbyte/ 2Mbye |
| LED | Power, LPT, Link/Act |
| Transport Protocol | TCP/IP, SMB, NetBEUI, AppleTalk |
| TCP/IP Protocol Supported | BOOTP, SNMP, Telnet, TFTP, FTP, LPD, RARP, DHCP, IPP |
| Supported OS | Windows 95/98(SE)/ME/NT/2000/XP/2003 Server Netware 5.x NDPS LPR Remote Printing (TCP/IP), HP-UX Unix, Sun OS, Solaris, SCO Unix, AIX, Unixware, Linux & Mac OS (AppleTalk) |
| Management | Windows Utility or Web-Browser Configuration |
| Power | 5V DC 2.5A External Power Adapter |
| Dimensions | 57 x 90 x 32mm (2.2 x 3.5 x 1.3 in.) Not Including Antenna |
| Weight | 85g (3.0 oz.) |
| Temperature | Operating: 0(C~50(C (32(F~122(F) Storage: -25(C~55(C (-13(F~131(F) |
| Humidity | 10%~90% (non-condensing) |
| Certification | CE, FCC |
| Wireless |
| Frequency | 2.4 ~ 2.4835 GHz (ISMB) |
| Encryption | 64/128-bit WEP (ASCII/HEX), WPA-PSK |
| Antenna | Detachable 2dBi Diversity Antenna (Reverse SMA Connector) |
| Data Rate (Auto Fallback) | 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps 802.11b: 11Mbps, 5.5Mbps, 2Mbps and 1Mbps |

Package Contents							Related Products

- TEW-P1PG								- TEW-432BRP

- Multi-Language Quick Installation Guide				- TEW-421PC

- Utility CD-ROM							- TEW-423PI

- Power Adapter (5V DC, 2.5A)

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

New Implements

- New Logo

54Mbps 802.11g Wireless 1-Port Parallel Print Server

TEW-P1PG is a print server that transforms virtually any stand-alone Parallel networkable printer into a shared network printer. The TEW-P1PG provides IEEE 802.11g 54Mbps wireless interface for integrating into existing wireless network. The TEW-P1PG is designed for printers equipped with parallel compliant printer port and it is an ideal network solution to convert conventional parallel printer into a shared resource on the network.

TEW-P1PG (Version B1.1R)