Features

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Wireless Devices

- IEEE 1284 Standard Male Centronics Bi-Directional Parallel Interface (DB-36)

- One RJ-45 10/100Mbps Auto-MDIX Fast Ethernet Port

- Supports Email Printing and FTP Printing

- Includes LPR Program for Windows 95/98/ME TCP/IP Printing

- Supports IPP Printing for Windows 2000/XP

- Supports UPnP (Universal Plug and Play) for Windows XP/2003

- Supports Mac 10.2 “Rendezvous” Zero-Configuration Function

- Latest MIB-II (RFC 1213) for SNMP Standard Management

- TCP/IP protocol supports SNMP, Telnet, TFTP, FTP, LPD, DHCP, BOOTP and IPP

- IP Assignment Support for DHCP, BOOTP and RARP

- Includes Windows-Based Administrative Program and Web-Based Configuration

- Built-in Flash Memory for Easy Firmware Upgrade and Configuration File Save & Restore

- Printing Access Control/Display and Email Notification for Printer Error Messages

- 3-Years Warranty

*Mac Systems are only compatible with Post-Script printers

Specifications

| Hardware |
| --- |
| Standards | Wired: IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX Wireless: IEEE 802.11g/b |
| Printer Interface | IEEE 1284 Male Centronics (DB-36) |
| LAN Port | 10/100Mbps Auto-Negotiation UTP/STP RJ-45 Port |
| CPU/ SDRAM / Flash ROM | RDC R2880 100MHz / 8MByte / 2MByte |
| LED | Power, LPT, Link/Act |
| Transport Protocol | TCP/IP, SMB, NetBEUI, AppleTalk |
| TCP/IP Protocol Supported | BOOTP, SNMP, Telnet, TFTP, FTP, LPD, RARP, DHCP, IPP |
| OS Support | Windows 95/98(SE)/ME/NT/2000/XP/2003 Netware 5.x NDPS LPR Remote Printing (TCP/IP) HP-UX Unix, Sun OS, Solaris, SCO Unix, AIX Unixware, Linux & Mac OS (AppleTalk) |
| Management | PS Utility or Web-Browser Configuration |
| Power | 5V DC 2.5A External Power Adapter |
| Dimensions | 90 x 52 x 30mm (3.5 x 2 x 1.25 inches) Not including antenna. |
| Weight | 70 g (2.5 oz.) |
| Temperature | Operating: 0(~50(C (32(~122(F) Storage: -25(~55(C (-13(~131(F) |
| Humidity | 10%~90% (non-condensing) |
| Certification | CE, FCC |
| Wireless |
| Frequency | 2.4 ~ 2.4835 GHz (Industrial Scientific Medical Band) |
| Module Technique | 802.11b: CCK (11 and 5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDN |
| Operating Mode/ Encryption | Ad-Hoc or Infrastructure / 64/128-Bit WEP, WPA |
| Antenna | 2dBi Detached Reverse-SMA (Male) Diversity Antenna (Length: 87mm/3.5inches) |
| Data Rate | IEEE 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps IEEE 802.11b: 11Mbps, 5.5Mbps, 2Mbps and 1Mbps (Auto Fallback) |
| Channel | 1~11 Channels (US Version) , 1~13 Channels (EU Version) |

TOP REASONS THE TEW-P1PG IS A LASTING TREND

| Integration Friendly | Supports multiple protocols and all popular Operating Systems. |
| --- | --- |
| Flexible | Integrates with 10Base-T, 100Base-TX or IEEE 802.11g/11b Wireless network. |
| Cost Effective | Turns the stand-alone printer into a network printer. |
| Performance | 54Mbps bandwidth for wireless network. |

Package Contents				Related Products

- TEW-P1PG					- TEW-P1UG

- Quick Installation Guide			- TEW-P21G

- Utility CD-ROM				- TE100-P1U

- Power Adapter (5V DC, 2.4A)			- TE100-P21

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

Official Site: www.TRENDnet.com

# Text boxes

54Mbps 802.11g Wireless Parallel Print Server

TRENDnet’s TEW-P1PG is a direct attached print server that transforms a stand-alone Parallel printer into a shared network printer. The TEW-P1PG provides IEEE 802.11g 54Mbps wireless interface for integrating into existing wireless network. The TEW-P1PG is designed for virtually all printers equipped with parallel compliant printer port and it is an ideal network solution to convert conventional parallel printer into a shared resource on the network.

TEW-P1PG

Front View

Back View

Network Solution for TEW-P1PG