FEATURES

- Compliant with IEEE 802.3ab 1000Base-T and IEEE 802.3z 1000Base-SX / 1000Base-LX Gigabit Ethernet Standards

- One 1000Base-T port with RJ-45 connector, supports full-duplex copper Gigabit connection

- One 1000Bse-SX or 1000Base-LX port that supports multi-mode or single-mode SC connector

- LED Indicators: Power, Link/Activity

- Extended single-mode fiber optic cable supports cable distance up to 50 Km (31.25 miles)

- Wall-Mountable

- Optional 19” system chassis with redundant power supply, holds up to 16 TFC series Media Converters

- 5-year Warranty

TREND SPEC’S

Standards:	IEEE 802.3ab 1000Base-T, IEEE 802.3z 1000Base-SX, IEEE 802.3z 1000Base-LX

Network Media:	1000Base-T:  CAT 5, EIA/TIA-568 100-ohm Screen Twisted Pair (STP), up to 100 meters. 1000Base-SX: 62.5/125um multi-mode fiber optic cable, up to 220 meters

50/125um multi-mode fiber optic cable, up to 550 meters

1000Base-LX: 62.5/125um multi-mode fiber optic cable, up to 550 meters

10/125um single-mode fiber optic cable, up to 50 km.

Protocol:	 CSMA/CD

Ports:	 1 x 1000Base-T, 1 x 1000Base-SX or 1000Base-LX

Data Transfer Rate:	 2000Mbps (Full-Duplex)

Diagnostic LEDs:	 Power, LINK/ACT

Power Adapter:	 7.5VDC/1.5A

Power Consumption: 7.2 Watts (max.)

Power Adapter:	 7.5VDC, 1.5A (7.2 watts max.)

Dimensions:	 120 x 88 x 25 mm (W x D x H)

Weight:	 Appro. 354 g. (12.5 Oz.)

Temperature:	 Operating: 0( ~ 40( C (32( ~ 104( F), Storage: -25( ~ 70( C (-13( ~ 158( F)

Humidity:	 Operating: 10% ~ 90%, Storage: 5% ~ 90% (non-condensing)

Certifications:	 FCC, CE, VCCI

TFC-1000MSC	1000Base-T to 1000Base-SX Multi-Mode Fiber with SC Connector

TFC-1000S10	1000Base-T to 1000Base-LX Single-Mode 10 km Fiber with SC Connector

TFC-1000S20		1000Base-T to 1000Base-LX Single-Mode 20 km Fiber with SC Connector

TFC-1000S50		1000Base-T to 1000Base-LX Single-Mode 50 km Fiber with SC Connector

TFC-1600	16-slot EIA-19” (2 Unit-Height) Chassis for TFC series Media Converters

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

Product

Information

TFC-1000 SERIES

TRENDnet’s TFC-1000 series Fiber Media Converter transforms 1000Base-T (Copper Gigabit) media to 1000Base-SX/LX (Fiber Gigabit) media and vice versa. The 1000Base-T port supports full-duplex Gigabit connection at wire speed with RJ45 connector. The fiber Gigabit connection supports shortwave (SX) or longwave (LX) laser optic with multi-mode or single-mode SC type connector. This converter will give your Copper Gigabit connection the ability to interface with fiber connection over a distance up to 50 Km. With the optional 16-slot EIA-19” rack-mount chassis, the TFC series converters are the perfect solutions for various fiber media conversions for your network.