FEATURES

- Compliant with IEEE 802.3 10Base-T and IEEE 802.3u 100Base-TX / 100Base-FX standards

- One 10/100Base-TX auto-negotiation RJ-45 port

- Auto-negotiation 10/100Mbps connection speed and half- / Full-duplex mode on TX port

- Auto MDI-X / MDI-II for 10/100Base-TX port

- One 100Mbps fiber port with Multi-mode SC, MT-RJ, or Single-mode SC connector

- Half- / Full-Duplex mode selector on Fiber port

- Status LED indicators for Power, Link/Activity, Full-Duplex, and Speed

- Wall-Mountable

- Optional 19” system chassis with redundant power supply, holds up to 16 TFC series Media Converters

- 5-year Warranty

TREND SPEC’S

Standards:		IEEE802.3 10Base-T, IEEE 802.3u 100Base-TX and 100Base-FX

Network Media:	100Base-TX: CAT 5, EIA/TIA-568 100-ohm UTP/STP, up to 100 meters.

100Base-FX: 50/125μm or 62.5/125μm multi-mode fiber optic cable, up to 2 Km.

9/125μm or 10/125μm single-mode fiber optic cable, up to 100 Km

Protocol:		CSMA/CD

Ports:		1 x 10/100Base-TX and 1 x 100Base-FX

Data Transfer Rate:	100Mbps (Half-Duplex), 200Mbps (Full-Duplex)

Diagnostic LEDs:	Power, Link/Activity, Full-Duplex, and Speed

Power Adapter:	7.5VDC, 1.5A (7.2 watts max.)

Dimensions:		120 x 88 x 25 mm (W x D x H)

Weight:		Appro. 354 g. (12.5 Oz.)

Temperature:		Operating: 0( ~ 40( C (32( ~ 104( F), Storage: -25( ~ 70( C (-13( ~ 158( F)

Humidity:		Operating: 10% ~ 90%, Storage: 5% ~ 90% (non-condensing)

Certifications:	FCC, CE, VCCI

TFC-110MST	10/100Base-TX to 100Base-FX Multi-Mode Fiber with ST Connector

TFC-110MSC	10/100Base-TX to 100Base-FX Multi-Mode Fiber with SC Connector

TFC-110MM	10/100Base-TX to 100Base-FX Multi-Mode Fiber with MT-RJ Connector

TFC-110S15	10/100Base-TX to 100Base-FX Single-Mode 15 km Fiber with SC Connector

TFC-110S30	10/100Base-TX to 100Base-FX Single-Mode 30 km Fiber with SC Connector

TFC-110S60	10/100Base-TX to 100Base-FX Single-Mode 60 km Fiber with SC Connector

TFC-110S100	10/100Base-TX to 100Base-FX Single-Mode 100 km Fiber with SC Connector

TFC-1600	16-slot EIA-19” (2 Unit-Height) Chassis for TFC series Media Converters

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

Product Information

TFC-110 SERIES

TRENDnet’s TFC-110 series Fiber Media Converter transforms 10/100Base-TX UTP/STP media to 100Base-FX media and vice versa. The 10/100Base-TX port auto-sense 10 or 100Mbps connection speed, auto-negotiates half-/full-duplex mode, and auto-selects MDI-X / MDI-II media type. The fiber connection can be multi-mode SC, MT-RJ, or single-mode SC Connector and it has a slide-switch for selecting half- or full-duplex mode.  This converter will give your Switch/Hub the ability to interface with fiber connection over a distance up to100 Km. With the optional 16-slot EIA-19” rack-mount chassis; the TFC series converters are the perfect solutions for various fiber media conversions for your network.