Features

- 3 x IEEE 1394 FireWire Port, Compliant with IEEE1394A Standard and Backward Compatible with IEEE 1394-1395 Devices

- 3 x USB 2.0 Type A Port, Compliant with USB 2.0 and USB 1.1 Specifications

- 32-bit 33Mhz Host Interface Compliant to PCI Specification 2.2

- OHCI 1.1 (Open Host Controller Interface) Compliant

- EHCI .95 (Enhanced Host Controller Interface) Compliant

- Provides High Speed USB Data Transfer Rate up to 480Mbps

- Provides High Speed FireWire Data Transfer Rate up to 400Mbps

- Provides Software Interrupt Control

- Supports up to 127 USB Devices

- Supports up to 63 FireWire Devices

- Compatible with Windows 98(SE)/ME/2000/XP Operating Systems

- Supports Plug & Play and Easy Installation

- 2-Year Warranty

Specifications				   Solution for TFU-H33PI

| Hardware |
| --- |
| Interface | 32-bit PCI rev. 2.2 |
| Standards | IEEE 1394A, 1394-1395 USB 2.0/1.1/1.0 |
| USB Controller | OHCI, EHCI |
| Ports | FireWire (6-pin IEEE 1394) 1 x Internal FireWire Port 2 x External FireWire Port USB 2.0 (Type A) 1 x Internal USB 2.0 Port 2 x External USB 2.0 Port |
| OS Compliant | Windows 98SE/ME/2000/XP |
| Data Rate | FireWire 100/200/400Mbps USB 2.0 - 1.5/12/480Mbps |
| Power Consumption | 500mA (max) per port |
| Dimensions (LxWxD) | 134 x 121 x 21.6mm (5.3 x 4.76 x 0.85 inches) |
| Weight | 66g (0.15lb) |
| Operating Temperature | 0( ~ 40( C (32( ~ 104( F) |
| Storage Temperature | -10( ~ 45( C (14( ~ 113( F) |
| Humidity | 0% ~ 85% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents		System Requirement

- TFU-H33PI			-    PC with Supported OS

- Quick Installation Guide		-    64MB RAM or More

- Driver CD-ROM			-    Available PCI Version 2.2 Slot

-    CD-ROM Drive for Driver Installation

# Text boxes

TFU-H33PI (v1.1R)

6-Port USB 2.0/FireWire Combo PCI Adapter

The 6-Port USB 2.0/FireWire Combo PCI Adapter provides your USB-enabled Desktop PC with a myriad of connections for peripherals. Its three USB 2.0 ports and three IEEE 1394 FireWire ports are perfect for connecting digital cameras, external hard-drives, printers, and other peripherals.