Features

- 4-Port DVI PS/2 and Audio KVM Switch with Enhanced Digital Video Support

- DVI-I Interface Technology Supports Pure Digital Video Signal Transmission

- Compatible with DVI-D (Digital Only) Connector

- Supports Microsoft IntelliMouse, InteiliMouse Explorer, Logitech NetMouse and more

- Enhanced Digital Video Support up to 1600 x 1200 High VGA Resolution

- Direct Channel Selection and Operation using Push Buttons or Hot-Key Commands

- Auto-Scan Mode for monitoring PCs and Beeping Sound for Switching Confirmation

- Numerical LED Display for Easy Monitoring ( One 7-Segment LED)

- Share Audio and Microphone between Multimedia PCs

- Supports DOC, Windows 95/98(SE)/ME/2000/XP, Linux and more

- Plug & Play and Hot-Pluggable

- EIA-19” (1U) Rack-Mountable (kit included)

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | DVI-I & DVI-D Compliant |
| PC Port Connector | 4 x PS/2 Keyboard 6-pin Mini Din (Female) 4 x PS/2 Mouse 6-pin Mini Din (Female) 4 x DVI-I Single Link (Female) |
| Console Port Connector | 1 x PS/2 Keyboard 6-pin Mini Din (Female) 1 x PS/2 Mouse 6-pin Mini Din (Female) 1 x DVI-I Single Link (Female) 1 x 3.5mm Audio in/out jack 1 x 3.5mm Microphone in/out jack |
| Cable 4 sets of DVI-I Dual Link KVM Cable (1.8m/6ft) | To KVM PS/2 Keyboard 6-pin Mini Din (Male) PS/2 Mouse 6-pin Mini Din (Male) DVI-I Dual Link (Male) To PC PS/2 Keyboard 6-pin Mini Din (Male) PS/2 Mouse 6-pin Mini Din (Male) DVI-I Dual Link (Male) Audio connector (Male) Microphone connector (Male) |
| PC Selection | Push Buttons or Hot-Key Commands |
| Keyboard/Mouse Emulation | PS/2 |
| Digital Display Resolution | 1600 x 1200 |
| Power | 9V DC, 1A External Power Adapter |
| Dimensions | 220 x 100 x 45mm (8.7 x 3.9 x 1.8 inches) |
| Weight | 1000 g (35.2 oz.) |
| Temperature | Operating: 0( ~ 40(C (32( ~104( F) Storage: -20( ~ 60(C (-4( ~ 140( F) |
| Humidity | 0%~90% RH, Non-Condensing |
| Certifications | FCC, CE |

TOP REASONS THE TK-404KR IS A LASTING TREND

| Integration Friendly | Does not require driver/software for the installation and operation. Switch between PCs with the push button or Hot-Key operation. |
| --- | --- |
| Flexible | Hot-Plug feature, add PCs or remove connected PCs without powering off the KVM switch or the other PCs. |
| Cost Effective | Manage two PCs with single keyboard, monitor, mouse and speakers/microphone. Save on equipment cost, utility, and space. |
| Performance | Support High Digital Video Quality up to 1600 x 1200. |

Package Contents				Related Products

- 4-Port DVI Audio KVM Switch			- TK-204K

- 4 sets of DVI-I Dual Link Cables

- Multi-Language User’s Guide

- Power Adapters (9V DC, 1A)

- Rack Mount Kit

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

4-Port Rack Mount DVI KVM Switch w/ Audio

TRENDnet’s TK-404KR 4-port DVI-KVM encompasses all your multimedia and multi-tasking needs into one cost effective solution.  Manage multiple PC’s effectively while enjoy audio-rich features with one set of LCD monitor, keyboard, mouse, microphone, and speakers.

#### TK-404KR

DVI KVM Switch Solution