Features

- Use one keyboard, monitor, and mouse to control four computer

- 4-Port PS/2 KVM switch with 1 set of Mic/Speaker port.

- 4 sets of PS/2, VGA and Audio & Microphone Cables

- Support Microsoft Intellimouse, Optical Mouse, Logitech Net Mouse and more

- Support very High Video Quality, up to 2048 x 1536 VGA resolution

- Support Windows 98(SE)/ME/2000/XP/2003 Server and Linux

- Hot-Plug feature, add PC or remove the connected PC for maintenance without powering down the KVM Switch or other PC’s.

- No software required, easy PC selection via Push Button or Hot-Key Commands

- Auto-Scan Mode for monitoring PC’s.

- Keyboard status restored when switching between PCs.

- LED display for easy status monitoring

- PS/2 Interface Power method

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Computer Connections | 4 |
| Cable | 4 sets of 1.8M (6ft.) KVM & Audio Cables |
| Cable Interface (All Male) | KVM Cable | To KVM | To PC |
|  |  | 1 x VGA/SVGA HDB 15-pin | 1 x PS/2 Keyboard 6-pin Mini Din 1 x PS/2 Mouse 6-pin Mini Din 1 X VGA/SVGA HDB 15-pin |
|  | Audio Cable | 1 x 3.5mm audio in/out jack 1 x 3.5mm microphone in/out jack | 1 x 3.5mm audio in/out jack 1 x 3.5mm microphone in/out jack |
| Console Connectors (All Female) | 1 x PS/2 Keyboard 6-pin Mini Din 1 x PS/2 mouse 6-pin Mini Din 1 x VGA/SVGA HDB 15-pin 1 x 3.5mm audio in/out jack 1 x 3.5mm microphone in/out jack |
| Port Selection | Push Buttons or Hot-Key Commands |
| Auto-Scan Interval | 5 seconds |
| Keyboard State | Saved and Restored |
| Power Type | PS/2 Interface Power |
| Dimensions | 167 x 80 x 28 (6.6 x 3.2 x 1.1in.) |
| Weight | 178g (6.3oz.) |
| Temperature | Operating: 0(C ~ 40(C (32(F ~104(F) Storage: -20(C ~ 60(C (-4(F ~140(F) |
| Humidity | 0%~90%, Non-Condensing |
| Certifications | CE, FCC |

Package Contents							Related Products

- TK-408								- TK-207K

- Multi-Language Quick Installation Guide		                          - TK-401R

- 4 sets of KVM & Audio Cables						- TK-210K

To order please call: 888-326-6061    Sales: sales@trendnet.com

Support: support@trendnet.com  Technical Support: (866) 845-3673

Official Site: www.trendnet.com

# Text boxes

# 4-Port PS/2 Audio KVM Switch Kit

The 4-Port PS/2 Audio KVM Switch lets you control multimedia PCs with just one keyboard, monitor, mouse, microphone, and a set of speakers. The KVM switch not only allows you to share your monitor, keyboard and mouse but you can also share microphone and speakers. With just a simple press of a button, this KVM switch eliminates the hassle of cable swapping and switching between 4 PCs. With it's Hot-Plug, Auto-Scan and Hot-Key operating features, the TK-408K is the perfect choice for managing 4 PCs. Separate KVM cables are included.

#### TK-408K (v1.0R)

Port Interface

KVM Solution with TK-408K