Features

- 2 x USB 2.0 type A port

- 32-bit CardBus PCMCIA type II slot compatible

- Compliant with USB 2.0 and USB 1.1 specifications

- Supports all USB speeds: low-speed (1.5Mbps), full-speed (12Mbps) and high-speed (480Mbps)

- OHCI 1.1 (Open Host Controller Interface) compliant

- EHCI .95 (Enhanced Host Controller Interface) compliant

- Switches to the peripheral’s highest supported speed automatically

- Fully f backward compatible with USB 1.1 devices

- Supports 6 layers with up to 127 USB devices

- Compatible with Windows 98SE/ME/2000/XP; Mac OS 10 or above

- Supports plug & play and easy installation

- 2-Year Warranty

Specifications					    Solution for TU2-H2PC

| Hardware |
| --- |
| Interface | 32-bit CardBus PCMCIA Type II |
| USB Controller | OHCI, EHCI |
| Standards | USB 2.0 & USB 1.1 |
| Ports | 2 x USB 2.0 Port |
| OS Compliant | Windows 98SE/ME/2000/XP Mac OS 10.x or higher |
| Data Rate | High-Speed: 480Mbps Full-Speed: 12Mbps Low-Speed: 1.5Mbps |
| Power Consumption | 500mA (max) per port |
| Dimensions (L x W x D) | 114 x 54 x12mm (4.4 x 2.1 x 0.5 in.) |
| Weight | 45g. (1.6oz.) |
| Operating Temperature | 0(C ~ 40(C (32(F ~ 104(F) |
| Storage Temperature | -10(C ~ 45(C (14(F ~ 113(F) |
| Humidity | 0 ~ 85% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents			    System Requirement

- TU2-H2PC				     -   Intel Pentium, 233MHz or above

- Multi-Language Quick Installation Guide	  -   Windows 98SE/ME/2000/XP

- Driver CD-ROM 			          Mac OS 10 or above

-   32MB RAM or more

# Text boxes

2-Port USB 2.0 Host PC Card

This 2-Port USB 2.0 Host PC Card gives your Laptop PC two USB 2.0 ports so you can easily connect your peripherals and enjoy the benefits of high-speed USB 2.0!

TU2-H2PC (v1.1R)