FEATURES

- Supports both ActiveX control for Internet Explorer and Java applet for Internet Explorer and Netscape Navigator

- Allows for remote access from web browser for live image viewing

- Supports TCP/IP networking, SMTP e-mail, HTTP and other Internet related protocols

- Utilized in a mixed operating system environment such as Windows and Macintosh

- Supports web configuration with password protection

- Supports both 10/100Mbps Ethernet/Fast Ethernet and IEEE 802.11b 11Mbps wireless networks

- Powerful Windows IP View Application Software for multiple cameras monitoring, image capturing, and video recording

- Two input connections for sensors/switches

- Two output connections for external devices for alarm based events when input sensor is triggered

- E-mail notification with captured images when input sensor is triggered

- Broad range of applications for monitoring homes, offices, banks, hospitals, and a variety of industrial and public monitoring

- 2-Year Warranty

TREND SPEC’S

TOP REASONS THE TV-IP200W IS A LASTING TREND

Integration Friendly:	Connects to 10Mbps, 100Mbps, or IEEE 802.11b 11Mbps wireless network

Economical:		Built-in web server; does not require additional computer and software

Flexible:		Install it in local area network or connect it to Internet for remote monitoring

Performance:		Color 640x480 pixels resolution with up to 30 frames per second video frame rate

TV-IP200W		Wireless Internet Camera Server

TV-IP200		Internet Camera Server

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

Product Information

T V-IP200W

TRENDnet's TV-IP200W Wireless Internet Camera Server is the perfect device for remote monitoring or transmitting real-time event over the Internet. With the reliability and scalability of IEEE 802.11b wireless and Fast Ethernet, the TV-IP200W functions as a video/surveillance camera allowing you to view live events with your web browser via Internet or Intranet. This Internet Camera Server has VGA quality video, automatic snapshot, event notification via e-mail, and auxiliary Input/Output connectors, making it the ideal solution for Internet video broadcasting applications.

| System Hardware |
| --- |
| LAN Connector: | RJ-45 10/100Mbps auto-sense |
| Generic I/O Port: | 2 x Inputs; 2 x Outputs (total 8-pin for 18AWG or smaller wires) |
| LED Indicator: | Power, LAN/WLAN Activity |
| Power Supply: | DC 5V, 2.4A switching type |
| Power Consumption: | 6.5 Watts (1300mA x 5V) |
| Physical / Environmental |
| Dimensions: | 170 x 85 x 46 mm (6.7 x 3.3 x 1.8 inches) |
| Weight: | 270 grams (9.5 Oz) |
| Temperature: | Operating: 5(C ~ 50(C (41(F ~ 122(F) |
|  | Storage: -25(C ~ 50(C (-13(F ~ 122(F) |
| Humidity: | 5% ~ 95% non-condensing |
| EMI: | FCC, CE, VCCI |

| Video Specification |  |
| --- | --- |
| Resolution: | 640 x 480 pixels |
| Image Sensor: | 1/3” color CMOS |
| Gain / Exposure / White Balance Control: | Automatic |
| Shutter: | Electronics 1/60 ~ 1/15000 sec |
| Minimum Illumination: | 2.5 lux @ f1.4, 3000K color |
| Focal Length: | 6.0 mm |
| Aperture: | F=1.8 |
| Focus Extent: | 20 cm ~ ∞ |
| Coverage Angle: | 56( |
| Lens mounting: | Fixed board lens, CS-mount type |

| Image (Video Setting) |  |
| --- | --- |
| Image Compression: | JPEG |
| Frame Rate: | 30fps@QCIF, 20fps@CIF, 3fps@VGA |
| Compression Rate Selection: | 5-level, (very low, low, medium, high, very high) |
| Frame Rate Setting: | 1, 5, 7, 15, 20, auto (depends on video format) |
| Video Resolution: | 160x120, 320x240, 640x480 |
| Brightness / Contrast / Hue Control: | Range 1 ~ 128 |

Communication Protocols

HTTP, FTP, TCP/IP, UDP, ARP, ICMP, BOOTP, RARP, DHCP, PPPoE

Hardware Requirements (minimum)

Pentium 200 CPU, 64MB RAM, 8MB free hard drive space, 800x600 resolution VGA video card, Ethernet Network Adapter or IEEE 802.11b Wireless Network Adapter

Software Requirements

Operating System: Windows 98, ME, 2000, XP, NT4.0, Mac OS 8 or above, Unix, or Linux

Web Browser: Web Browser with Active X or Java enabled

Remote Management Software (included): IP View , runs with Windows 98, ME, 2000, XP, and NT4.0

| Wireless Specification |  |
| --- | --- |
| Wireless Standard: | IEEE 802.11b |
| Data Rate: | 1, 2, 5.5, 11 (Mbps) |
| Module Technique: | DSSS (Direct Sequence Spread Spectrum) |
| Antenna: | Internal Patch Antenna with diversity |
| Frequency: | 2.4 ~ 2.4835Ghz (ISMB) |

| Wireless Specification (continued) |
| --- |
| Output Power: | 17 dBm (typical) |
| Receiving Power: | 10-5 BER @ -84 dBm (11Mbps) min. |
| Channels: | 11 (US & Canada) |
| Network Architecture: | Ad-Hoc (peer-to-peer) or Infrastructure (with Access Point) |

###### Internet Camera Solutions for TV-IP200W