Features

- Compliant with Bluetooth v2.0 Specification with EDR (Enhanced Data Rate) support

- Backward compatible with Bluetooth v1.1 and v1.2 devices

- Compliant with Class I Bluetooth Operations

- Support Full-Speed Bluetooth operation with Full Piconet support

- Support Graphical LCD display with status Indicators

- Support Long Life Lithium Rechargeable Battery

- Headset support for voice communication such as Skype, MSN Messenger, Yahoo Messenger and more

- Full Skype support allows users to use Skype features directly from the phone (such as SkypeIn™ calls, SkypeOut™, Status change, Conference Call and etc.)

- Compatible with Windows Windows 2000/XP Operating Systems

- ClearSky Long Range Support up to 100 meters (328 ft.) (depends on the environment)

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | Class I Bluetooth v2.0 with EDR Backward Compatible with Bluetooth v1.1, v1.2 |
| Headset Interface | Mini-B USB Connector for charging Earphone Jack (2.5mm) Built-in Speakerphone |
| Adapter Interface | USB 1.1, 2.0 / External Dipole Antenna |
| Display | 96 x 64 pixel (STN LCD with back light) |
| LED Indicator | Headset Status (Active, Standby, Sleep) |
| Battery | 3.6V 700mAh Lithium-ion Rechargeable Battery |
| Cable | Type A to Mini-B USB Cable (1m / 3ft.) for charging |
| Power Consumption | Standby Time : 60+ hours Talk Time : 6+ hours |
| Dimensions | Headset: 143.5 x 45 x 22 mm (5.6 x 1.78 x 0.9 in.) Adapter: 71.25 x 35.6 x 11.25 mm (2.8 x 1.4 x 0.44 in.) |
| Unit Weight | Headset: 100 g (3.5 oz.) / Adapter: 10 g (0.35 oz.) |
| Temperature | Operation: 0(~ 50(C (32(F~122(F); Storage: -20(~ 70(C (-4(F~158(F) |
| Humidity | 10~90% |
| Certification | CE, FCC |
| Phone Features |  |
| Volume | Volume up: Vol +; Volume down: Vol - |
| Skype Support | - Sync Contact list, History, SkypeIn, SkyOut - Conference Call, Skype Credit Status - Support Status Change (Online, Offline, Skype Me, Away, Not Available, Do not Disturb and Invisible) |
| Bluetooth |  |
| Frequency | 2.4 ~ 2.4835 GHz ISM Band |
| Spread Spectrum | Frequency Hopping and Adaptive Frequency Hopping |
| RF Output Power | 17dBm (typical) |
| Receiving Sensitivity | -90dBm@0.1%BER ( typical ) |
| Date Range | Up to 100m (328 ft.) depends on environment |

Package Contents			Related Products

- TVP-SP1B				- TBW-101UB

- TBW-104UB				- TBW-102UB

- Lithium-ion Rechargeable Battery	- TBW-103UB

- Multi-Language Quick Installation Guide

- CD-ROM (Driver/User’s Guide)

- USB Cable (1m/3 ft.)

To order please call: 888-326-6061 • Sales: sales@trendware.com

Support: techsupport@trendware.com • Tech Support Hotline: 1(310) 626-6252

Official Site: www.TRENDnet.com

# Text boxes

TVP-SP1BK

ClearSky ™ Bluetooth VoIP Phone Kit (for Skype™)

The ClearSky Bluetooth VoIp Phone provides a cost effective solution that allows you to make phone calls anywhere around the world. Streamline calling procedures by taking advantage of SkypeTM features such as Contacts, Call List, SkypeOut, and Conference Call. The rechargeable Lithium-ion battery can also sustain 6 hours of conversation.