Features

- Hands-free with speaker-out support, dedicated for conference call in office

- Supports Mute feature

- Built-in high performance microphone and mono speaker

- Echo-cancellation function provides superior sound quality

- Compliant with VoIP solution or instant message software such as Skype, Yahoo Messenger & MSN Messenger

- LCD display for caller ID, contact list, calling list with backlight support

- Supports Multi-Language display and Hot-Key functions for easy control

- Compliant with Windows 98SE/ME/2000/XP

- Plug & Play

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standard | USB 1.1 |
| Interface | 1 x USB Type B (Female) port 1 x 3.5mm Stereo Jack (headset) 1 x 3.5mm Microphone Jack (microphone) 1 x 5V DC in (for optional power adapter) |
| Solution | 8 Bits DSP Voice processing Echo-cancellation: up to 45dB Audio output frequency range: 44.1KHz Audio input sampling rate: 8KHz, 8 bits |
| Built-in Speaker | 41 x 71mm Response Frequency: 100Hz~20KHz Output Impedance: 1W/8Ohm |
| Built-in Microphone | Sensitivity: -40 ± 2dB Directivity: Omni Directional Response Frequency: 50Hz ~ 16KHz |
| Response Frequency | 100Hz ~ 15K Hz |
| Signal-To-Noise Ratio | More than 60dB |
| Receiver Output Impedance | 2.2KOhm |
| Operating Voltage | DC 5V (Bus-Powered) |
| LCD | Resolution: 128 x 64 pixels Size: 32 x 19.7mm Backlight: enabled Multiple Language Display: enabled |
| Operating Temperature | 0( ~ 40( C (32( ~ 104( F) |
| Humidity | <95% (Non-Condensing) |
| Emissions | FCC, CE |

System Requirements

- Computer with one available USB 1.1 port or higher

- To use Skye with the USB speaker unit, your computer must meet the following minimum requirement.

  - PC running Windows 2000 or XP

  - 400MHz Processor

  - 128MB RAM

  - 15MB free disk space

  - Working Internet connection

  - With provided utility installed.

Package Contents				Related Products

- TVP-SP2					- TVP-SP1BK

- Multi-Language Quick Installation Guide

- USB Cable

- Utility CD-ROM

# To order please call: 1-888-326-6061 (USA)

## Sales: sales@trendnet.com  • Support: techsupport@trendnet.com

www.TRENDnet.com

# Text boxes

VoIP USB Speakerphone (forSkype™)

The USB Speakerphone allows you to use the Internet to make free hands-free conference calls.   It is compatible with the leading Skype™, and instant messaging applications such as MSN™ & Yahoo™ Messanger.  The USB Speakerphone utilizes advanced VoIP technology to deliver a cost-effective alternative to standard telephony solutions.

TVP-SP2 (v1.0R)