Features

- Compliant with Bluetooth v2.0 Specification with EDR (Enhanced Data Rate) support

- Backward compatible with Bluetooth v1.1 and v1.2 devices

- Compliant with Class I Bluetooth Operations

- Advanced acoustic echo cancellation technology and Superior noise suppression

- Support Full-Speed Bluetooth operation with Full Piconet support

- Support Graphical LCD display with status Indicators

- Headset support for voice communication such as Skype, MSN Messenger, and Yahoo Messenger

- Full Skype support allows users to use Skype features directly from the phone (such as SkypeIn™ calls, SkypeOut™, Status change, Conference Call and etc.)

- Compatible with Windows 2000/XP Operating Systems

- Multi-Language LCD User Interface Support (English, French, German, Spanish & Italian)

- ClearSky Long Range Support up to 100 meters (328 ft.) (depends on the environment)

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | Class I Bluetooth v2.0 with EDR Backward Compatible with Bluetooth v1.1, v1.2 |
| Interface | Mini-B USB Connector for charging 3 built-in mono microphone 1 built-in mono speaker |
| Adapter Interface | USB 1.1, 2.0 / External Dipole Antenna |
| Display | 128 x 80 pixel (STN LCD with back light) |
| LED Indicator | Power, MIC enable, Mute, Online |
| Battery | 3.7V 650mAh Lithium-ion Rechargeable Battery (built-in) |
| Cable | Type A to Mini-B USB Cable (1m / 3ft.) for charging |
| Power Consumption | Normal Mode: 30 days. Stand by Mode : 72+ hours, Talk Time : 4+ hours |
| Dimensions | Bridge: 242 x 242 x 54 mm (9.5 x 9.5 x 2.1 in.) Adapter: 71.25 x 35.6 x 11.25 mm (2.8 x 1.4 x 0.44 in.) |
| Unit Weight | Bridge: 0.5kg (1.1lb) / Adapter: 10 g (0.35 oz.) |
| Temperature | Operation: 0(~ 50(C (32(F~122(F); Storage: -20(~ 70(C (-4(F~158(F) |
| Humidity | 10~90% |
| Certifications | CE, FCC |
| Phone Features |  |
| Volume | Volume up: Vol +; Volume down: Vol -; Mute |
| Skype Support | - Sync Contact list, History, SkypeIn, SkyOut - Conference Call, Skype Credit Status - Support Status Change (Online, Offline, Skype Me, Away, Not Available, Do not Disturb and Invisible) |
| Bluetooth |  |
| Frequency | 2.4 ~ 2.4835 GHz ISM Band |
| Spread Spectrum | Frequency Hopping and Adaptive Frequency Hopping |
| RF Output Power | 17dBm (typical) |
| Receiving Sensitivity | -90dBm@0.1%BER ( typical ) |
| Date Range | Up to 100m (328 ft.) depends on environment |

Package Contents				Related Products

- TVP-SP4B				 	- TVP-SP1BK

- TBW-104UB					- TVP-SP2

- Multi-Language Quick Installation Guide	- TVP-SP3

- CD-ROM (Driver/User’s Guide)

- USB Cable (1m/3 ft.)

To order please call: 866-845-3673 • Sales: sales@trendnet.com

Support: support@trendnet.com • Tech Support Hotline: 1(310) 626-6252

Official Site: www.TRENDnet.com

# Text boxes

miniUSB Connector

TVP-SP4BK (v1.0R)

ClearSky ™ Bluetooth VoIP Conference Phone Kit

The ClearSky™ VoIP Bluetooth Conference Phone Kit allows you to hold quality conference calls through a Bluetooth connection.  Advanced echo cancellation technology and superior noise suppression design provides a business quality conferencing experience.  This Bluetooth Class I device can easily hold conference calls wirelessly up to 100 meters away.

MIC1

Antenna

Speakerphone

Mute LED

MIC1 LED

Bluetooth LED

Power LED

MIC2 LED

MIC 2

MIC 3

MIC3 LED

LCD:128 x 80