## Features

- Built-in 3 x 10/100Mbps Auto-MDIX Ports

- Built-in 1 x 10/100Mbps WAN Port and 1 x 10/100Mbps DMZ Port

- Supports Cable/DSL Modems with Dynamic IP, Static (Fixed) IP, PPPoE, PPTP, or L2TP Connection Types

- Compliant with Windows 95/98/ME/NT/2000/XP, Unix, and Mac System

- Supports up to 10 IPSec Tunnels

- Supports 100 (IPSec, L2TP, PPTP) Pass-Through Sessions Simultaneously (when each VPN client connects to a different VPN endpoint)

- Supports PPTP 1 Server and 10 Clients (Microsoft VPN) VPN Connections

- Website Access Restriction using URL Keywords (50 entries) and Special Application Access

- Provides Virtual Servers(Port Forwarding) and Services Type Control with up to 60 Firewall Rules

- Provides Access Control with user define Services Types (70 entries)

- Provides Static Routing, Dynamic DNS Service, Hardware DMZ, and Software Multi-DMZ

- ALGs (Application Level Gateways) with Special Application Support (6 entries) and UPnP (Universal Plug & Play) Support

- Supports Network Address Translation (NAT/NAPT) and Stateful Packet Inspection (SPI) Firewall

- Real-Time Email Alert and Logs (Incoming, Outgoing, System, and VPN)

- Easy Web Browser (HTTP) Configuration and Remote Management (HTTPS)

- Flash Memory for Firmware Upgrade and Save/Restore Router Configuration

- 5-Year Warranty

## Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 (10-Base T), 802.3u (100-Base TX) |
| Protocols | NAT, PPPoE, NTP, SMTP, HTTP, TFTP, DHCP, TCP/IP, PAP, CHAP, RIP1, RIP2, DDNS |
| WAN | 1 x 10/100Mbps Port (Internet) |
| LAN | 3 x 10/100Mbps Auto-MDIX Ports |
| DMZ | 1 x 10/100Mbps Auto-MDIX Port |
| LED Indicators | Unit: Power, Status LAN Ports/DMZ Port: Link/Act, 100 |
| Power Adapter | 9V DC, 700mA |
| Dimensions (L x W x H) | 141 x 100 x 27 mm (5.5x 3.9 x 1.06 inches) |
| Weight | 0.36 kg (12.8 oz.) |
| Temperature | Operating: 0˚ to 40˚ C (32˚ to 104˚ F) Storage: -10˚ to 70˚ C (14˚ to 158˚ F) |
| Humidity | Operating: 0 % ~ 80 % (non-condensing) Storage: 0% ~ 95% (non-condensing) |
| Certifications | FCC, CE, VCCI |
| Router |
| Firewall | NAT Firewall, SPI Firewall |
| Security | URL Filter, Access Control, Password Protection, Email Alert and Logs |
| VPN (IPSec) | MD5-HMAC/SHA1-HMAC Authentication, DES-CBC, 3DES-CBC encryption, Internet Key Exchange, Manual Key Negotiation |
| VPN Tunnels | 10 (IPsec), 10 (PPTP) |
| VPN Pass-Through | IPSec, PPTP, L2TP (100 Sessions) |

### TOP REASONS THE TW100-BRV204 IS A LASTING TREND

| Easy Integration | With the built-in 10/100Mbps Switch, you can integrate this device to any Ethernet/Fast Ethernet Network |
| --- | --- |
| Cost-Effectiveness | Share the broadband Internet connection, saves router costs and account charges |
| Security | Firewall protection keeps hackers out |
| Performance | Experience the high speed Internet access while reducing network traffic |

Product Information

TW100-BRV204	Cable/DSL VPN Firewall Router

TW100-BRV304	Cable/DSL Advanced VPN Firewall Router

TW100-BRF114	Cable/DSL Firewall Router

TW100-S4W1CA	Cable/DSL Broadband Router

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

TW100-BRV204 (v2)

Cable/DSL VPN Firewall Router

TRENDnet’s TW100-BRV204 Cable/DSL VPN Firewall Router provides a remote workforce or branch office shared broadband internet access, while providing advanced Firewall and VPN security against potential hacker attacks. In addition to Network Address Translation (NAT), the router includes a robust Stateful Packet Inspection Firewall (SPI) to filter traffic at the packet level with protection against the popular Denial of Service (DoS) attacks. VPN encryption supports up to 10 VPN tunnels via client pc-to-endpoint or endpoint-to-endpoint configuration. The install wizard helps make installation and VPN set-up quick and easy. The new VPN Firewall family delivers advanced security for your sensitive information at an affordable price.

Network Solution for TW100-BRV204

Front Panel

Back Panel