Model: 15-AH28B (H/W: A1)

Features

- Additional heat insulation

- Aluminum construction

- External use

- Flip open top

- Require additional equipments for cable installation

- 1 Year Warranty

Specification

| ITEMS | 15-AH28B (H/W: A1) |
| --- | --- |
| Housing Size | L mm W mm H mm | 440 (17”) |
|  |  | 139 (5.5”) |
|  |  | 119 (4.7”) |
| Max Camera Size | L mm W mm H mm | 195 (7.7”) |
|  |  | 70 (2.75”) |
|  |  | 70 (2.75”) |
| Weight | 2kg (4.55lb) |
| Clear Window Area | Ψ78 |
| Glass | 3mm |
| Housing Material | Aluminum |
| Finish | Light Gray Powder – coating Body, Black End Caps |
| Proposal | Outdoor |
| Heater | Turn on at 5℃±2℃, Turn off at 10℃±2℃ |
| Fan | Turn on When Power in |
| Power Supply | 90 ~ 230V AC |

Supported Models

- TV-IP100 / TV-IP100W

- TV-IP201 / TV-IP201W

- TV-IP301 / TV-IP301W

Ps. Cameras need to use the Camera’s own power adapter

Heavy Duty Bracket

- Cable for camera can be run through centre of bracket for anti tamper protection

- Max Load: 10 kg.

- Construction: Steel

- Fixing: 4 screws

- Height: 230 mm

- Swivel Angle: 90ﾟ

- Tilt Angle: 120ﾟ

- Weight: 4.7kg (10.5lb)

- Dimension: 6.7 x 3 x 48 cm (2.6 x 1.2 x 19 inches)

# Text boxes

Camera Housing

15-AH25B

Camera Housing

15-AH25B