Features

- Weather resistant IP66 protection certified

- Protects PTZ (Pan/Tilt/Zoom) camera from dust, rain, and snow.

- Build-in power supply, blower and heater to keep the front window clear of moisture and frost

- Holds most indoor PTZ camera non-weatherproof cameras to outdoor use.

- Automatic Thermostatic control: heater “On” under  -10(C (14(F) “OFF” over 0(C (32(F), Fan “On” under 45(C (113(F) ”OFF” over 40(C (104(F)

- Heavy duty Gooseneck and Straight tube pendent brackets for easy wall or ceiling mounting

- Cables are routed inside the mounting bracket

- 2 Years Warranty

Specifications

| Hardware |
| --- |
| Range of Application | Indoor/ Outdoor Installations |
| Protection Level | IP66 Weatherproof |
| Blower Fan and Heater | Heater ON: under -10(C (14(F) OFF: over 0(C (32(F) Blower Fan ON: under 45(C (113(F) OFF: over 40(C (104(F) |
| Housing Material | Steel |
| Power Supply | 110/220AC 24V Input, 12VDC Output |
| Housing Dimensions | 215 (d) x 390mm (8.5(d) x 15.4in.) |
| Inside Dimension | 125 x 170 x 130mm (4.9 x 6.7 x 5.1in.) |
| Weight | Housing: 4.9kg(10.8lb) Bracket: 3.0kg (6.6lb) |
| Temperature | -25(C ~ 50(C (-13(F ~122(F) |
| Humidity | 0%~90%, Non-Condensing |

Package Contents							Related Products

- EL-HS800								- TV-IP400

- Mounting Bracket							- TV-IP400W

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: support@trendnet.com•  Tech Support Hotline: (888)777-1550

Official Site: www.trendnet.com

# Text boxes

# Outdoor Dome Housing with Fan/Heater

The TRENDnet EL-HS800 provides the perfect solution to transform regular PTZ (Pan/Tilt/Zoom) cameras into outdoor surveillance systems.  Made from steel and designed for high level of protection (IP66), the EL-HS800 completely shields cameras from dust, water and snow.  It also comes complete with an adjustable fully-cable-managed mounting bracket, protecting camera wiring from the weather.

#### EL-HS800

* Camera sold separately