les

Features

- Compliant with Bluetooth v2.0 Specification with EDR (Enhanced Data Rate) support

- Backward compatible with Bluetooth v1.1 and v1.2 devices

- Support Full-Speed Bluetooth operation with Full Piconet support

- Support AFH (Adaptive Frequency Hopping) and Fast Connection

- Up to 3Mbps Access Data Rate and Low Power Consumption

- Compatible with Windows 2000/XP & MCE (Media Center Edition) Operating Systems

- Enable computers to connect Bluetooth enabled devices such as printers, headset, audio/video, basic Image, PDAs, and mobile phones

- Compliant with Class I Bluetooth Operations

- Communicates wirelessly up to 100 meters (328 ft.) (depends on the environment)

- Trouble free Plug-n-Play Installation

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | Class I Bluetooth v2.0 with EDR Backward Compatible with Bluetooth v1.1, v1.2 USB 1.1, 2.0 |
| Antenna | External Dipole Antenna |
| Supported OS | Windows 2000/XP & MCE |
| Power Consumption | Typical: 95mA; idle: 12mA Tx max: 136mA @19dBm; Rx max: 45mA |
| Dimensions | 71.25 x 35.60 x 11.25 mm (2.8 x 1.4 x 0.44 in.) |
| Weights | 10 g (0.35 oz.) |
| Temperature | Operation: 0(~ 50(C (32(F~122(F) Storage: -20(~ 70(C (-4(F~158(F) |
| Humidity | 10~90% |
| Emissions | CE, FCC |
| Bluetooth |  |
| Frequency | 2.4 ~ 2.4835 GHz ISM Band |
| Spread Spectrum | Frequency Hopping and Adaptive Frequency Hopping |
| Module Technique | GFSK, DQPSK(2Mbps) and 8DPSK(3Mbps) |
| Profile Support | DUN (Dial-up Networking), FAX LAP (LAN Access Profile), SPP (Serial Port Profile) HID (Human Interface Device), HCRP (Hardcopy Cable Replacement Profile) FTP (File Transfer Profile), OPP (Object Push Profile) A2DP (Advanced Audio Distribution Profile), GAVDP (Generic Audio/Video Distribution Profile) HSP (Headset Profile), PAN (Personal Area Networking) BIP (Basic Image Profile), SYNC (Synchronization Profile) AV (Audio Video), GOEP (Generic Object Exchange Profile) |
| RF Output Power | 17dBm (typical) |
| Receiving Sensitivity | -90dBm@0.1%BER (typical ) |
| Data Rate | Up to 3Mbps |
| Data Range | Up to 100m (328 ft.) depends on environment |

Package Contents			Related Products

- TBW-104UB 				- TVP-SP1BK

- Quick Installation Guide		- TBW-101UB

- CD-ROM (Driver/User’s Guide)		- TBW-102UB

- USB Cable (15cm/6 in) 		- TBW-103UB

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: techsupport@trendnet.com • Tech Support Hotline: 1(866)845-3673

Official Site: www.TRENDnet.com

# Text boxes

Advanced High-Speed Bluetooth USB 2.0 Adapter

The USB 2.0 Bluetooth Adapter allows you to make wireless connections between your computer and Bluetooth-enabled devices. This Bluetooth v2.0 utilizes Enhanced Data Rate (EDR) to allow for data rates up to 3Mbps. The Bluetooth adapter can easily connect to your Bluetooth-enabled devices from up to 100 meters away.

TBW-104UB (v2.0R)