les

Features

- Compliant with Bluetooth v2.0 Specification with EDR (Enhanced Data Rate) support

- Backward compatible with Bluetooth v1.1 and v1.2 devices

- Support Full-Speed Bluetooth operation with Full Piconet support

- Support AFH (Adaptive Frequency Hopping) and Fast Connection – enhanced inquiry scan (immediate RHS response), LMP improvements, Parameter Ranges, Extended SCO (eSCO) SCO handle, Synchronization

- Support Scatternet and up to 7 active slave devices

- Up to 3Mbps Access Data Rate and Low Power Consumption

- Compatible with Windows 98SE/ME/2000/XP Operating Systems

- Enable computers to connect Bluetooth enabled devices such as printers, headset, audio/video, basic Image, PDAs, and mobile phones

- Compliant with Class II Bluetooth Operations

- Communicates wirelessly up to 10 meters (32.8 ft.) (depends on the environment)

- Trouble free Plug-n-Play Installation

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | Class II Bluetooth v2.0 with EDR Backward Compatible with Bluetooth v1.1, v1.2 USB 2.0 |
| Antenna | Internal printed antenna |
| Supported OS | Windows 98SE/ME/2000/XP |
| Power Consumption | Typical: 95mA; idle: 12mA Tx max: 136mA @19dBm; Rx max: 45mA |
| Dimensions | 47 x 18 x 8 mm (1.85 x 0.7 x 0.3 in.) |
| Weights | 5g (0.18oz.) |
| Temperature | Operation: 0(~ 40(C (32(F~104(F) Storage: -10(~ 65(C (14(F~149(F) |
| Humidity | 5%~95%RH (no condensation) |
| Emissions | CE, FCC |
| Bluetooth |  |
| Frequency | 2.4 ~ 2.4835 GHz ISM Band |
| Module Technique | GFSK (Gaussian Frequency Shift Keying). π/4 DQPSK, 8DPSK |
| Profile Support | DUN (Dial-up Networking), FAX, BPP ( Basic Printing Profile) LAP (LAN Access Profile), SPP (Serial Port Profile), GAP (Generic Access Profile) HID (Human Interface Device), HCRP (Hardcopy Cable Replacement Profile) FTP (File Transfer Profile), OPP (Object Push Profile) A2DP (Advanced Audio Distribution Profile), GAVDP (Generic Audio/Video Distribution Profile) HSP (Headset Profile), PAN (Personal Area Networking) BIP (Basic Image Profile), SYNC (Synchronization Profile) AV (Audio Video), GOEP (Generic Object Exchange Profile) |
| RF Output Power | 4dBm (typical) |
| Receiving Sensitivity | -86dBm@0.1%BER (typical ) |
| Data Rate | Basic data rate: up to 723.2Kbps Enhanced data rate: up to 3Mbps |
| Data Range | Up to 10m (32.8 ft.) depends on environment |

Package Contents			Related Products

- TBW-105UB 				- TVP-SP1BK

- Quick Installation Guide		- TBW-101UB

- CD-ROM (Driver/User’s Guide)		- TBW-102UB

- TBW-103UB

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: techsupport@trendnet.com • Tech Support Hotline: 1(866)845-3673

Official Site: www.TRENDnet.com

# Text boxes

TBW-105UB (v1.0R)

Compact Bluetooth USB 2.0 Adapter

The USB Bluetooth Adapter allows you to make short-range wireless connections between your computer and Bluetooth-enabled devices. This Bluetooth v2.0 utilizes Enhanced Data Rate (EDR) to allow for data rates up to 3Mbps. The Bluetooth adapter can easily connect to your Bluetooth-enabled devices from up to 10 meters away.