## FEATURES

- Tests Pin Configuration of 10/100/1000Base-T, 10Base-2 (coax), RJ-11/RJ-12/RJ-45, EIA/TIA-356A/568A/568B, and Token Ring Cables

- Tests USB and IEEE 1394 cables with optional adapters

- Built-in Tone Generator for tracing cable with standard Tone Probe

- LED display

- Tests the grounding on shielded (screened) cable

- Verifies cable continuity, opens, shorts, and miswires

- Tests cable up to 300 meters (984 feet)

- Auto-Scan or Manual-Scan mode

- Includes Deluxe Carrying Pouch, two RJ-45-to-BNC Adapters, and RJ-45 Patch Cable

- 1-year warranty

TREND’S SPECS

Power Requirement: 	One DC 9V battery

Tone Frequency: 	600 ~ 800 Hz.

Dimensions (appr.):	Master Unit: 116 x 68 x 28 mm (4.57 x 2.7 x 1.1 inch)

Remote Terminator: 118 x 32 x 27 mm (4.6 x 1.3 x 1.1 inch)

Operating Temp:	0° C ~ 45° C (32° F ~ 113° F)

Weight (appr.): 	Master Unit:  113 gram (4 Oz.) (without battery)

Remote Terminator: 57 gram (2 Oz.)

## PRODUCT INFORMATION

| TC-NT2 | Network Cable Tester with Tone Generator for UTP, STP, Coaxial, and Modular Cables |
| --- | --- |
| TC-CT68 | RJ-11/RJ-45 Crimp/Cut/Strip Tool |
| TC-PDT | Punch Down Tool with 110 and Krone Blade |
| TC-1KC5G | 100MHz CAT 5 Solid Cable/1,000 Feet Box |

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

Professional Cable Tester with Tone Generator

The TC-NT2 is a convenient and comprehensive cable tester for network professionals. Its powerful and user-friendly features enable network installers to accurately check pin configurations of various voice and data communication cables. The TC-NT2 includes a master unit that transmits test signals to its corresponding remote terminator to verify cable reliability. It checks continuity and displays wiring configuration up to 300 meters of cable installation. With the unique feature of the audio tone generator, the TC-NT2 identifies and troubleshoots faulty cables to assure proper pin and wiring structure.

TC-NT2