## FEATURES

- Complies with IEEE 802.3μ 100Base-FX standard

- Meets PCI Specification Rev. 2.2

- 32-bit PCI Bus Master operation

- 100Mbps Fast Ethernet connection

- Supports half- and full-duplex modes

- Supports 2Km fiber cable long transfer distance

- Auto-assignment of IRQ and I/O address

- Easy-to-view diagnostic LEDs

- Supports Wake-On-LAN (WOL). 3-wire WOL cable included

- Supports Desktop Management Interface (DMI)

- 5-years warranty

TREND SPEC’S

Standard:			IEEE 802.3μ 100Base-FX

Data Transfer Rate:	100Mbps (half-duplex) / 200Mbps (full-duplex)

Protocol:	CSMA/CD

Connectors:	Multimode SC fiber connector

Diagnostic LEDs:	Link and Activity

Network Drivers:	Novell Netware 3.x/4.x, ODI driver, NetWare Client 32, Windows for Workgroups(, Windows 95/98/2000/NT, IBM OS/2 Warp Server, Linux, NDIS driver, and other major network operating systems

Power Consumption:	5 VDC, 700mA Max.

Dimensions:	135 x 121 mm (5.31 x 4.76 inches)

Weight:	85 g (3 oz)

Operating Temp.: 	0° to 40° C  (32° F to 104° F)

Storage Temp.:	-25° to 70° C  ( -13°F to 158° F)

Humidity:	10 % to 90 % (non-condensing)

Certifications:            	FCC, CE, VCC1

### TOP REASONS THE TE100-PCIFXplus  IS A LASTING TREND

Performance:	 Operates in the 32-bit bus master mode, and transfers data directly to/from the host’s memory.

Easy Installation: Uses standard SC type fiber connector for easy and reliable connection.

Flexibility:	 Supports all major network operating systems.

Reliability:        	 With 100/200Mbps speeds, our TE100-PCIFXplus offers a lifetime warranty.

TE100-PCIFXplus	100Base-FX Fast Ethernet Fiber Adapter for PCI

TE100-S88FX		8-Port 100Base-FX Fast Ethernet Switch

TE100-S86FX		8-port (6 x 100Base-FX, 2 x 10/100Mbps) Fast Ethernet Switch

TE100-S81FX		6-port (1 x 100Base-FX, 7 x 10/100Mbps) Fast Ethernet Switch

TE100-TF		100Base-TX to 100Base-FX SC-type converter

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

TE100-PCIFXplus

PRODUCT

INFORMATION

100Base-FX SC Connector PCI

Fast Ethernet Fiber Adapter

The PCI Fiber Optic Adapter operates in a 32-bit Bus Master Mode, delivering 100Mbps of speed with little stress on the host’s CPU.  The TE100-PCIFXplus supports both half- and full-duplex modes, creating an increase speed up to 200Mbps.   With it’s SC-type fiber connection allowing up to 2Km away from the switch, TRENDnet’s TE100-PCIFXplus is the perfect choice for greater bandwidth and long cable connections in the network.

PRODUCT

INFORMATION

Fast Ethernet Solutions for TE100-PCIFXplus