Features

- Compliant with IEEE 802.3 10Base-T, IEEE 802.3µ 100Base-TX

- 16 x 10/100Mbps Auto Negotiation and Auto-MIDX ports

- Supports Store and Forward Switching architecture with non-blocking full wire-speed performance

- Full/Half Duplex Transfer Mode for Each Port

- Wire-Speed Filtering/Forwarding Rates

- IEEE 802.3x Flow Control for Full-Duplex Mode

- Backpressure Flow Control for Half-Duplex Mode

- Integrate Address Look-Up Engine, Supports up to 8K Absolute MAC Address

- 512kbytes Internal RAM for Frame Buffering

- Extensive Front-Panel Diagnostic LEDs

- Plug and Play Design

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3μ 100Base-TX ANSI/IEEE 802.3 Auto-Negotiation |
| Protocol | CSMA/CD |
| Connectors | 16 10/100Mbps Auto-MDIX RJ45 Ports |
| Cabling | Cat. 3,4,5 UTP/STP for 10Base-T Cat. 5 UTP/STP for 100Base-TX |
| Data Transfer Rate | 10Mbps: 10/20Mbps (Half/Full Duplex) 100Mbps: 100/200Mbps (Half/Full Duplex) |
| Diagnostic LEDs | Power, 10 Link/Act, 100Link/Act, FDX, COL |
| Power | 7.5V DC, 1A External Power Adapter |
| Power Consumption | 25 watts max. |
| Dimensions (L X W X H) | 184 x 124x 44mm (7.2” x 4.9” x 1.7”) |
| Weight | 848 g (1.87 lb) |
| Temperature | Operating: 0(C ~ 40(C (32(F ~ 104(F) Storage: -10(C to 70(C (14(F to 158(F) |
| Humidity | Operating: 10 % ~ 90 % (non-condensing) Storage: 5 % ~ 90 %(non-condensing) |
| Certifications | FCC, CE |

TOP REASONS THE TE100-S16Eplus IS A LASTING TREND

| Integration Friendly | Easily upgrade to Fast Ethernet without changing switch |
| --- | --- |
| Economical | Provides 10/100Mbps of Fast Ethernet in the same unit |
| Flexible | The Auto-MDIX ports automatically negotiate between 10Base-T and 100Base-Tx network speeds between half/full modes |
| Performance | Supports store and forward switching architecture with non-blocking full wire-speed performance |

Package Contents	Related Product

- TE100-S16Eplus					- TE100-S55Eplus

- Multi-Language User’s Guide				- TE100-S88Eplus

- Power Adapter (7.5V DC, 1A)				- TE100-S16

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252  Official Site: www.TRENDNET.com

# Text boxes

Network Solution for TE100-S16Eplus

16-Port 10/100Mbps Fast Ethernet Switch

TRENDnet’s TE100-S16Eplus is an auto-sensing switch that designed specifically to boost network performance by eliminating network congestions and unnecessary network traffics.  Each port on the switch provides dedicated bandwidth and can negotiate between 10Mbps and 100Mbps network speeds. Desktop size design for easy storing and installation.

TE100-S16Eplus (c1)