Features

- 24 10/100Mbps Auto-Negotiation, Auto-MEDIX Fast Ethernet RJ-45 Ports

- Compliant with IEEE 802.3 / IEEE 802.3u Standards

- Provides 2Mbits RAM for Data Buffering

- Supports 8Kbytes MAC Address Entries

- Compliant with Windows, Linux, and Mac Operating Systems

- IEEE 802.3x Flow Control

- Store-and-Forward Switching Method

- Broadcast Storm Protection

- Non-blocking Architecture

- Max 4.8Gbps Switching Capacity

- Diagnostic LEDs

- Plug & Play

- 19” (1U) Rack Mount Design

- 5-Years Warranty

Specifications

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX |
| Interface | 24 10/100Mbps Auto-MDIX RJ-45 Ports |
| Network Media | Ethernet: UTP/STP Cat. 3,4,5 Fast Ethernet: UTP/STP Cat. 5 |
| Switch Fabric | 4.8Gbps Forwarding Capacity |
| Data Transfer Rate | Ethernet: 10Mbps/20Mbps (Half/Full Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full Duplex) |
| Data RAM Buffering | 2Mbits per device |
| SSRAM | 1.25Mbits |
| MAC Table | 8Mbytes or 4096 Entries Per Device |
| Protocol | CSMA/CD |
| Transmission Method | Store-and-Forward |
| Power | 100-240VAC, 50/60H, Internal Power Supply |
| Power Consumption | 7.5 Watts (Max) |
| Diagnostic LED | Power, Link/ACT, 100Mbps |
| Weight | 1.54kg (3.4.1lb) |
| Dimensions (W x H x D) | 280 x 180 x 45mm (11 x 7.09 x 1.77 in.) |
| Temperature | Operating: 0(C ~ 50(C (32(F ~ 122(F) Storage: -20(C ~ 70(C (-4(F ~ 158(F) |
| Humidity | Operating: 10 % ~ 90 % (Non-Condensing) Storage: 5 % ~ 90 %(Non-Condensing) |
| Certification | CE, FCC |

Package Contents						Related Product

- TE100-S24R							- TE100-S5

- Multi-Language Quick Installation Guide			- TE100-S88Eplus

- Power Cord							- TE100-S16R

- Rack Mount Kit

To order please call: 888-326-6061 • Sales: sales@trendnet.com
Support: support@trendnet.com • Tech Support Hotline: (866)845-3673

www.trendnet.com

# Text boxes

24-Port 10/100Mbps Fast Ethernet Switch

This 24-Port 10/100 switch is a high performance auto-sensing switch that automatically negotiates between 10Base-T and 100Base-TX network speeds. All ports support full/half-duplex mode for maximum network performance. Designed and built to increase network bandwidth, this 24-Port 10/100 switch is the best solution for both corporate and small business network environments.

TE100-S24R (H/W: v1.0R)