Features

- 8 x 10/100Mbps Auto-MDIX Ports

- Supports switch Fabric up to 3.8GBps

- Layer 2 Management Switch with Full Software Support

- IGMP Snooping with Query Mode Support for Multi-Media Application

- Supports Broadcast Storm Filtering

- Supports Port Status Control (Status, Auto-Negotiation, Speed, Duplex and Flow Control)

- Supports Port Trunking with Flexible Load Distribution Control and Fail-Over Functions

- Supports Port-Based VLAN and IEEE 802.1Q Tag-Based VLAN

- Supports IP Multicast, Port Mirroring, Spanning Tree, SNMP and RMON

- Supports Port Security and IEEE 802.1p Class of Services

- Store-and-Forward Switching Architecture with Non-Blocking Wire-Speed Performance

- Configuration via RS-232 Console Port, Telnet, and Web Browser (HTTP)

- TFTP Firmware Upgrade via Browser

- Configuration File Save and Restore Support

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T Ethernet; IEEE 802.3u 100Base-TX Fast Ethernet IEEE 802.3x Flow Control; IEEE 802.1D Spanning Tree IEEE 802.1q Tag-based VLAN; IEEE 802.1p Class of Service IEEE 802.3ad Link Aggregation |
| Interface | 8 x 10/100Mbps Auto-MDIX RJ45 Fast Ethernet Port |
| Packet Forwarding and Filtering Rate | 100M Ethernet: 148,800 packets per second per port 10M Ethernet: 14,880 packets per second per port |
| Cabling | Fast Ethernet: UTP/STP Cat. 5, EIA/TIA-568 100-ohm, 100 meters max |
| Console Port | RS-232, female 9-Pin Serial Port (M-M serial cable included) |
| Protocol/Topology | (CSMA/CD) / Star |
| Buffer Memory | 2Mbits Data Buffer |
| Filtering Address Table | 8K MAC Address Entries |
| Bandwidth | Up to 3.8Gbps |
| LED Display | Power, Link/Activity, Full Duplex/Collision |
| Power | Input: 100~240VAC, 50/60Hz Internal Power Supply |
| Power Consumption | 17 watts |
| Dimensions | 250 x 133 x 37mm (9.8 x 5.2 x 1.5 inch) (W x H x D) |
| Weight | 1.08 Kg. (2.4 lb.) |
| Temperature | Operating: 0( ~ 45( C (32( ~ 113( F) Storage: -40( ~ 70( C (-40( ~ 158( F) |
| Humidity | 10% ~ 90% non-condensing |
| Safety Emissions | FCC, CE |
| Software |
| Management | Web Management, RS-232 Console Management, Telnet |
| Trunk | Max 4 Groups ( up to 4 ports per group) |
| Class of Service | Supports High and Low Priority |
| QoS | Supports 8 Levels of Priority and Mapping to High/Low Priority Queue for Class of Service |
| VLAN | Up to 256 VLAN groups and up to 4094 VLAN ID |
| IP Multicast | IGMP Snooping up to 256 groups 2 Types of Query Mode: Enable/Disable or Auto Query |
| Filter Database | Port Static MAC address lock, MAC filter and Port Security |
| Port Mirror | Up to 8 ports |
| Broadcast Control | None, 5%, 10%, 15%, 20%, 25% |
| Spanning Tree | IEEE 802.1d Support |
| RFC Standard | RFC 768 UDP, RFC 783 TFTP, RDC791 IP, RFC 792 ICMP, RFC 854 TELNET Server/Client, RFC 1112 IGMP, RFC 2068 HTTP, RFC 2674 VLAN MID, RFC 1493 Bridge MIB, RFC 1157 SNMP, RFC 1213 MIB II, Bridge MIB, RFC 1643 Ethernet Like, RFC 1757 RMON1, LANTECH Enterprise MIB, RFC 1215 Trap |

Packaging Contents			Related Products

- TE100-S800i			- TE100-S810Fi

- CD-Rom(User’s Guide)		- TEG-081Fi

- Quick Installation Guide

- RS-232 Cable / Power Cord

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310) 626-6252    www.TRENDNET.com

# Text boxes

8-Port 10/100Mbps Layer 2 Managed Switch

The 8-Port 10/100Mbps Layer 2 Managed Switch provides exceptional performance, ease of use and flexibility for managing business networks. Utilizing a robust 3.8Gbps backplane, the 8 port managed switch can connect to multiple switches while handling full-duplex operations.  In addition to the switch’s scalability, it also offers a variety of management features such as SNMP, IGMP for multi-media applications, VLAN, Port Security, Spanning Tree Protocol, Port Trunking, Broadcast Storm Filtering, Port Mirroring and other features that can easily be accessed through a web browser or a command line interface.

TE100-S800i

Management Switch Network Solution