Features

- 24 10/100Mbps Auto-negotiation, Auto-MDIX Fast Ethernet Ports

- 2 Pairs of 10/100/1000mbps Gigabit Copper Port and Mini-GBIC Slot

- Full/Half duplex mode for each port (Full Duplex Mode only for Gigabit Ports)

- Store and Forward switching method

- Integrated address Look-Up Engine with 8K absolute MAC address table

- Supports 256Kbytes RAM Data Buffering

- Extensive diagnostic LED’s on the front panel

- IEEE 802.3x flow control for full-duplex mode

- Back pressure flow control for half-duplex mode

- Easy configuration the device from a Web browser

- Supports Port-Based VLAN, Port-Based QoS and IEEE 802.1p QoS

- Supports Trunking (3 trunk groups) and Port Mirroring

- Supports Port Based Bandwidth Rate Control (Ingress / Egress Rate)

- Support Port setting function allow user setting each port’s speed, duplex mode, and flow control

- Standard 19” (1U) Rack-mount design

- 5-Years Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3ab 1000Base-T IEEE 802.3z 1000Base-SX/LX (Mini-GBIC) IEEE 802.3x Full Duplex Flow Control |
| Network Media | Ethernet: UTP/STP Cat. 3, 4, 5 Fast Ethernet: UTP/STP Cat. 5 Gigabit: UTP/STP Cat. 5, 5E, 6 Mini-GBIC: LC Type Fiber Optic |
| Protocol /Topology | CSMA/CD, Star |
| Interface | 24 x 10/100Mbps Auto-MDIX Fast Ethernet ports 2 pairs x 1000-Based RJ45 Port and Mini-GBIC Slot* * One RJ45 Port or Mini-GBIC Slot of each pair can be used at a time. |
| Data Transfer Rate | Ethernet: 10Mbps/20Mbps (Half-Duplex/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half-Duplex/Full-Duplex) Gigabit Ethernet: 2000Mbps (Full-Duplex) |
| Address Table | 8K Entries |
| Data RAM Buffer | 256KBytes |
| Diagnostic LEDs | Per Unit: Power, System Per Gigabit Ethernet: Link/ACT, Speed Per Cooper Gigabit Port: Link/ACT, Speed 100M, Speed 1000M, Mini-GBIC |
| Power/Consumption | 100-240V AC, 50/60Hz Internal Power Supply / 11 Watts (max) |
| Dimensions (W x D x H) | 440 x 140 x 44 mm (17.32 x 5.5 x 1.73 inches) |
| Weight | 2.1kg (4.7 lbs) |
| Temperature | Operating : 0( C ~ 40( C (32( F ~ 104( F) Storage: -10( C ~ 70( C (14( F ~ 158( F) |
| Humidity | Operating: 10% ~ 90% RH Storage: 5% ~ 90% RH |
| Safety Emissions | FCC, CE |

Package Content						Related Product

- TEG-224WSplus					- TEG-160WS

- Quick Installation Guide					- TEG-240WS

- Utility CD-ROM						- TEG-2248WS

- Power Cord

- Rack-Mount Kit

## To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • TEL: (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

www.TRENDNET.com

# Text boxes

New Implements

- Added shared Mini-GBIC ports

- New TRENDnet housing/mylar

- RoHS compliant unit

TEG-224WSplus

26-Port Gigabit Web Smart Switch

TEG-224WSplus 26-port Web-Based Smart Switch is the ideal Switch for network segmenting and flexibility. It has 24 10/100Mbps, 2 10/100/1000Mbps ports and 2 Mini-GBIC slots. TEG-224WSplus supports web browser configuration allowing Network Administrators to configure speed, VLAN, QoS, Trunking and Mirroring down to the port level. TEG-224WSplus is powerful, easy-to-use and enhances network security.