## Features

- PCMCIA CardBus 68-pin Connector Type II Card

- 32-Bit Bus-Mastering Data Transfer

- 10/100/1000Mbps Data Rate Auto-Negotiation Operation

- Built-in Transmit 8K/Receive 64K Bytes RAM Data Buffer

- Supports Full-Duplex Mode Doubles Network Data Rate to 20/200/2000Mbp

- Supports Windows 98SE/ME/2000/XP

- Ultra Low Power Consumption

- Supports IEEE 802.3x Flow Control

- Supports IEEE 802.1Q VLAN Tagging (Windows 2000 and XP only)

- Supports Promiscuous Mode

- Compatible with Extensive Notebook Models

- Supports Hot Swap and True Plug-and-Play

- 5-Years Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10BASE-T Ethernet IEEE 802.3u 100BASE-TX Fast Ethernet IEEE 802.3ab 1000Base-T Gigabit ANSI/IEEE 802.3 Auto-Negotiation PCMCIA 2.x |
| Network Media | Ethernet: UTP Cat. 3, 4, 5, EIA/TIA-568 100-ohm STP Fast Ethernet: UTP Cat. 5, EIA/TIA-568 100-ohm STP Gigabit: UTP Cat. 5, 5E, 6 EIA/TIA-568 100-ohm STP |
| Protocol | CSMA/CD |
| Interface | 32-Bit CardBus Type II |
| Dimension | 120 x 53 x 3mm (4.7 x 2 x 0.1 inches) |
| Power Consumption | 3.3V DC |
| Diagnostic LED | Link/Activity Speed |
| Supported Drivers | Windows 98SE/ME/2000/XP |
| Data Rate | Ethernet: 10Mbps/20Mbps (Half/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full-Duplex) Gigabit: 2000Mbps(Full Duplex) |
| Temperature | Operating: 0° ~ 40° C (32° ~ 104° F) Storage: -10° ~ 70° C (14° ~ 158° F) |
| Humidity | Operating: 10%~90% (Non-Condensing) Storage: 5%~90% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents

- TEG-PCBUSR

- Multi-Language Quick Installation Guide

- Driver & User’s Guide CD-ROM

##### To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310) 626-6252

Official Site: www.TRENDnet.com

# Text boxes

TEG-PCBUSR (v1.1R)

10/100/1000Mbps Gigabit CardBus PC Card

TEG-PCBUSR transforms your laptop PCs into powerful Gigabit workstations. The TEG-PCBUSR features latest 1000Mbps technology and it is fully compatible with existing 10/100Mbps networks. The TEG-PCBUSR dramatically improves network performance up to 2000Mbps with switched full-duplex operations. Mobile users can now incorporate Gigabit Ethernet with the TEG-PCBUSR.

Related Products

- TEG-S50TXE

- TEG-S80TXE

- TEG-PCITXR