FEATURES

- 24 x 10/100Mbps Auto-negotiation MDIX Fast Ethernet Ports

- 2 x 10/100/1000Mbps Auto-negotiation, Auto-MDIX Gigabit Ports

- Full/Half duplex mode for each port (Full Duplex only for Gigabit Ports)

- Store and Forward switching method

- Integrated address Look-Up Engine with 8K absolute MAC address table

- Supports 2.5MB RAM data buffering

- IEEE 802.3x flow control for Full Duplex mode

- Back pressure flow control for Half Duplex mode

- Extensive Front-Panel Diagnostic LEDs

- Standard 19” Rack-mount design

- 5-Years Warranty

# TECH SPEC’S

LAN Standards:	IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX, IEEE 802.3ab 1000Base-T,. IEEE 802.3x Full Duplex Flow Control

Network Media:	     		Ethernet: UTP/STP Cat. 3, 4, 5

Fast Ethernet: UTP/STP Cat. 5

Gigabit : UTP/STP Cat. 5, Cat 5E (Recommend)

Protocol:			CSMA/CD

Topology:			Star

LAN Port:		24 x 10/100Mbps Auto Negotiation, Auto-MDIX Fast Ethernet ports,

2 x 10/100/1000Mbps Auto Negotiation, Auto MDIX Gigabit ports

Address Table:	      		8K entries per device

Data RAM buffer			2.5MB per device

Data Transfer Rate:		Ethernet:  10/20Mbps – Half/Full-Duplex

Fast Ethernet:  100/200Mbps – Half/Full Duplex

Gigabit Ethernet: 2000Mbps – Full Duplex

Diagnostic LEDs:		Per Unit: Power System

Per Fast Ethernet Port: Link/ACT, 100M (port 1~24)

Per Gigabit Ethernet Port: Link/ACT, 1000M, 100M (port 25, 26)

Power Consumption:      		11.75 Watts. Max

Power Supply:			100-240V AC, 50/60Hz Internal Universal Power Supply

Dimensions:     			440 x 140 x 44 mm (17.32"  x 5.5" x 1.73")

Weight:				4.7 lb

Operating Temperature:  		0( ~ 40( C (32( ~ 104( F)

Storage Temperature: 		-10( ~ 70( C (14( ~ 158( F)

Humidity:		10% ~ 90% (no-condensing)

Certifications:		FCC Class A, CE Mark A, VCCI-A

TOP REASONS THE TEG-S224 IS A LASTING TREND

Easy Upgrade: 	Ethernet workgroups are able to upgrade to Fast Ethernet by changing adapters and a hub without changing switches.

Expandability: 	Simple expansion by uplinking to 10/100Mbps or Gigabit Switches

Performance:            	Provides non-blocking high performance with internal switch controller.

Cost-Effectiveness:   	The TEG-S224 presents Gigabit Ethernet at an affordable rate.

TEG-S224	26-Port 10/100/1000Mbps Copper Gigabit Switch(Rack Mount)

TEG-S18TXE	9-Port (8 10/100, 1 10/100/1000) Copper Gigabit Mini Switch

TEG-S80TXD	8-Port Copper Gigabit Switch

## To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • TEL: (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

Product Information

TEG-S224

26-port 10/100/1000Mbps Copper Gigabit Switch

TRENDnet's TEG-S224 is a 26-port 10/100/1000Mbps Gigabit Ethernet Switch with 24 10/100Mbps Fast Ethernet ports and 2 10/100/1000Mbps Copper Gigabit Ethernet ports. Users can connect Servers to the Gigabit port(s) to increase network performance or uplink Copper Gigabit Switches together to create a high-bandwidth Gigabit backbone. TRENDnet's TEG-S224 provides simple migration, scalability and flexibility to handle new applications and data types making it a highly reliable and cost effective solution for high-speed network connectivity.

Network Solution for

TEG-S224