Features

- Stackable up to 16 Switches with Gigabit Ports

  - Single IP function supports up to 32 Switches

  - Single IP management with stackable mode (Gigabit ports only)

  - Single IP management with agent mode (Any port on the switch)

- Manage all Uplink or Stacked Switches Locally or Remotely with a Single IP Address

  - Public IP required when managing remotely; Port 80/28019 need to be opened when running behind a Firewall/Router

- 24 10/100Mbps Auto-Negotiation Ethernet/Fast Ethernet Ports

- 1 Gigabit Module Slot; supports the following optional Modules: 1-Port 100Base-FX, 2-Port 100Base-FX, 2-Port Copper Gigabit, 1-Port Fiber Gigabit, 2-Port Fiber Gigabit, or 1-Port Copper Gigabit + 1-Port GBIC

- Built-in 3Mb Packet Buffer and 1Mb Control Buffer

- Provides 6K MAC, 4K VLAN and 2K Multicast Entries

- Supports 255 Entries of Static MAC and Port Based MAC Table Display

- Supports 802.3x Flow Control for Both Half/Full Duplex Operation

- Supports Head-of-Line Blocking Prevention

- Supports Broadcast Storm Filtering

- Supports Port-Based VLAN (256 Groups), IEEE 802.1Q Tag-Based VLAN (PVID 1~255)

- Supports 802.1v Protocol-Based VLAN Classification

- Supports 802.1x Authentication and Authorization

- Supports IP Multicast, IGMP Snooping and 802.1D Spanning Tree

- Supports 2-Level Priority Queuing

- Supports Port Trunking with Flexible Load Distribution Control and Fail-Over Functions

  - Max 7 Trunk groups with 4 ports per group

- Supports Ingress Port Security Mode and By-Port Egress/Ingress Rate Control

- Supports Source-Port-Based, Destination-Port-Based, and Source-Destination-Pair-Based Sniffer Function

- Supports RMON Group 1, 2, 3, 9 and PING Function from the Switch

- Store-and-Forward Switching Architecture with Non-Blocking Wire-Speed Performance

- Configuration via Console Port (serial cable included), SNMP (v1.0, MIB II), TELNET, and Web Browser

- Upgradable Firmware via Browser with TFTP Program

- Standard 19” (1U) Rack Mount Size (kit included)

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T Ethernet IEEE 802.3u 100Base-TX Fast Ethernet IEEE 802.3z 1000Base-SX/LX Gigabit Ethernet IEEE 802.3x Flow Control IEEE 802.1D Spanning Tree IEEE 802.1q Tag-based VLAN, Priority Control IEEE 802.1v Protocol-Based VLAN IEEE 802.1x Authentication and Authorization IEEE 802.3ad Link Aggregation |
| Interfaces | 24 x 10/100Mbps Auto-MDIX RJ45 Fast Ethernet Port 1 x Gigabit Slot (optional Gigabit Copper or Fiber Modules) |
| Packet Forwarding and Filtering Rate | 1000M Ethernet: 1,488,000 packets per second per port 100M Ethernet: 148,800 packets per second per port 10M Ethernet: 14,880 packets per second per port |
| Cabling | Fast Ethernet: UTP/STP Cat. 5, EIA/TIA-568 100-ohm, 100 meters max 62.5/125um Multimode Fiber with SC-type connector, 2Km max. Gigabit Ethernet: UTP/STP Cat. 5, 5E, 6, EIA/TIA-568 100-ohm, 100 meters max 62.5/125μm Multimode Fiber with SC-type connector, 220 meters max. 50/125μm Multimode Fiber with SC-type connector, 550 meters max. |
| Console Port | RS-232, female 9-Pin Serial Port (M-M serial cable included) |
| Protocol/Topology | (CSMA/CD) / Star |
| Buffer Memory | 1Mb for Control, 3Mb for Packet Filter |
| Filtering Address Table | 6K MAC (255 entry of Static MAC), 4K VLAN and 2K Multicast Entries |
| LED Display | Power On(Green)/Off(Off) Diagnostic (Blinking) during Initialization Link(Green)/Activity(Blinking) Speed 100M(Green)/10M(Off) Gigabit Port: 1000Mbps(Green)/Activity(Blinking) |
| Power | Input: 100~240VAC, 50/60Hz Internal Power Supply |
| Power Consumption | 30 watts max. |
| Dimensions | 440 x 184 x 44mm (17.3 x 7.3 x 1.8 inch) (W x H x D) |
| Weight | 2.5 Kg. (5.2 lb.) |
| Temperature | Operating: 5( ~ 45( C (41( ~ 113( F) Storage: -20( ~ 70( C (-4( ~ 158( F) |
| Humidity | 10% ~ 90% non-condensing |
| Certifications/Safety | FCC, CE |

Packaging Contents			Related Products

- TEG-S2400i			- TEG-S2600i

- Quick Installation Guide

- CD-ROM (User’s Guide)

- Power Cord

- RS-232 Cable

- Rack Mount Kit

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hotline: (888)777-1550

www.trendnet.com

# Text boxes

24-Port SNMP Stackable Switch

The TEG-S2400i 24 Port Stackable SNMP switch provides foundation for a highly scalable and easily managed network. The Web/SNMP Managed Switch allows network administrators to remotely monitor and manage network performance and security. Network administrators can stack up to 16 switches and manage them with a single IP address. The TEG-S2400i can be incorporated into high-speed backbone connectivity through Gigabit ports or mini-GBIC ports. Security and performance are optimized with advanced features including Port/Tag-based VLAN, QoS, and Trunking.

TEG-S2400i (h/w: 1.2)

### Optional Modules

- TEG-S24M100F

(1-Port Multimode SC-type 100Base-FX Module)

- TEG-S24M200F

(2-Port Multimode SC-type 100Base-FX Module)

- TEG-S24M2C

(2-Port 10/100/1000 Copper Gigabit Module)

- TEG-S24M1F

(1-Port Multimode SC-type Fiber Gigabit Module)

- TEG-S24M2F

(2-Port Multimode SC-type Fiber Gigabit Module)

- TEG-S24M11GF

(1-Port 10/100/1000Mbps Copper Gigabit + 1-Port 1000Base-SX multimode SC type Module)