Features

- Compliant with IEEE 802.3ab or IEEE 802.3z Gigabit Standards

- Modules: Gigabit Copper (TEG-S3M2CG), Mini-GBIC (TEG-S3M2MG), and Gigabit Copper and Fiber Combo (TEG-S3M11CF)

- Optional Gigabit Modules for TEG-S3000i (Layer 2 Managed Chassis Switch)

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3ab Gigabit Copper IEEE 802.3z Gigabit fiber for SX and LX IEEE 802.3x Flow Control and Back Pressure |
| Interface | TEG-S3M2CG : 2 x 10/100/1000Mbps Auto-MDIX RJ-45 Port TEG-S3M2MG : 2 x 3.3v Mini-GBIC Slot TEG-S3M11CF : 1 x 10/100/1000Mbps Auto-MDIX RJ-45 Port 1 x 1000Base-SX Multi-Mode SC Type Fiber Port |
| LED | Link/Activity, 100Mbps, 1000Mbps, Full Duplex, GBIC Fiber |
| Cable Parameters | Gigabit Copper: Cat.5 or Cat.6 4-paris UTP Cables, up to 100m Mini-GBIC: LC Type. 62.5/125μm or 50/125μm Multi-Mode Fiber Optic cable (SX) LC Type. 9/125μm or 10/125μm Single-Mode Fiber Optic cable (LX) Gigabit SX : 50/125um or 62.5/125um Multi-Mode Fiber Optic, up to 550m (wavelength: 850nm) |
| Dimensions | 84 x 88 x 30mm (3.3 x 3.5 x 1.2 in.) |
| Weight | 200g (7.3 oz.) |
| Temperature | Operating: 0(~45(C (32(~113(F) Storage: -10(~70(C (14(~158(F) |
| Humidity | 10%~90% (non-condensing) |
| Certification | CE, FCC |

Package Contents					Related Products

- TEG-S3M2CG/TEG-S3M2MG/TEG-S3M11CF		- TEG-S33000i												- TEG-S3M8TX / TEG-S3M8FX / TEG-S3M8S15

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support:  techsupport@trendnet.com Tech Support Hot Line: 888-777-1550

Official Site: www.trendnet.com

# Text boxes

TEG-S3M2MG

TEG-S3M11CF

TEG-S3M2CG