Features

- Compliant IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX and IEEE 802.3x Flow Control

- 8 x 10/100Mbps Auto-Negotiating and Auto-MDIX RJ-45 Ports

- Optional Modules for TEG-S3000i (Layer 2 Managed Chassis Switch)

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 :10Base-T IEEE 802.3u : 100Base-TX IEEE 802.3x : Flow Control |
| Interface | 8 10/100Mbps Auto-MDIX Fast Ethernet RJ-45 Ports |
| Switch Architecture | Store/Forward |
| LED | Link, Activity, Full-duplex |
| Data Transfer Rate | Ethernet: 14880pps Fast Ethernet: 148800pps |
| Network Cable | Ethernet: Cat. 3,4,5 Fast Ethernet: Cat. 5 |
| Protocol | CSMA/CD |
| Dimensions | 126 x 46 x 35mm (5.0 x 1.8 x 1.4 in.) |
| Weight | 213g (7.6oz.) |
| Temperature | Operating: 0(~45(C (32(~113(F) Storage: -10(~70(C (14(~158(F) |
| Humidity | 10%~90% (non-condensing) |
| Certification | CE, FCC |

Package Contents			Related Products

- TEG-S3M8TX				- TEG-S3000i		- TEG-S3M2CG

- TEG-S3M8FX		- TEG-S3M2MG

- TEG-S3M8S15	- TEG-S3M11CF

To order please call: 888-326-6061 • Sales: sales@trendnet.com  • 
Support:  techsupport@trendnet.com • Tech Support Hot Line: 888-777-1550

Official Site: www.trendnet.com

# Text boxes

TEG-S3M8TX

8-Port 10/100Mbps Module