Features

- 5 10/100/1000Mbps Auto-Negotiation, Auto-MDIX Gigabit RJ-45 ports

- Compliant with IEEE 802.3 / IEEE 802.3u standards

- IEEE 802.3x Flow Control support

- Provide 4K MAC address entries

- Supports Jumbo Frame of up to 9728bytes packet size

- Compliant with Windows, Linux, and Mac Operating Systems

- Store-and-Forward Switching method

- Non-blocking Architecture

- Diagnostic LEDs

- Plug & Play

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3x Flow Control |
| Network Media | Ethernet: UTP/STP Cat. 3,4,5, EIA/TIA-568 100-ohm Fast Ethernet: UTP/STP Cat. 5. 5E, EIA/TIA-568 100-ohm |
| Data Rate | Ethernet: 10Mbps/20Mbps (Half/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full-Duplex) Gigabit: 2000Mbps (Full-Duplex) |
| Switch Fabric | 10Gbps Forwarding Capacity |
| Topology | Star |
| Interface | 5 10/100/1000Mbps Auto-MDIX RJ-45 Ports |
| Filtering Table | 4K entries per device |
| Buffer Memory | 8Kbytes per device |
| Power Consumption | 5.6 watts (max) |
| Diagnostic LED | Power, Link/ACT, 100Mbps/1000Mbps |
| Power Adapter | Switching Power 5VDC 2.5A / Linear Power 12VDC 1A |
| Dimension | 150 x 105 x 33mm (5.9 x 4.1 x 1.3 inches) |
| Weight | 225g (8 oz) |
| Temperature | Operating: 0° ~ 50° C (32° ~ 122° F) |
| Humidity | 10%~90% (Non-Condensing) |
| Certification | CE, FCC |

Package Contents						Related Products

- TEG-S5							- TEG-PCITXR

- Multi-Language Quick Installation Guide			- TEG-PCBUSR

- Power Adapter 						- TEG-S8

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: support@trendnet.com • Technical Support: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

5-Port 10/100/1000Mbps Gigabit Switch

TEG-S5 is an Auto-MDIX switch designed specifically to boost network performance by eliminating network congestions and unnecessary network traffics.  Each port on the Switch provides dedicated bandwidth and can negotiate between 10/100/1000Mbps network speeds and half/full duplex modes. Plug and Play provides cost-effective and high performance solutions.

#### TEG-S5 (v1.0R)