Features

- 8 x 10/100/1000Mbps Auto-Negotiation, Auto-MDIX Gigabit Ethernet Ports

- Full/Half-duplex transfer mode for 10/100Mbps, Full-Duplex mode for 1000Mbps

- Store-and-Forward switching method

- Wire-speed reception and transmission

- IEEE 802.3x flow control for full-duplex mode

- Back pressure flow control for half-duplex mode

- Integrated address Look-Up engine, supports 8K MAC addresses table

- Operates and maximizes packet filtering and forwarding rate

- Provides 144kbyte RAM data buffering

- Sturdy metal housing

- Diagnostic LEDs

- Plug & Play

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3ab 1000Base-T |
| Network Media | Ethernet: 2-pair UTP Cat. 3,4,5, 100 meters max Fast Ethernet: 2-pair UTP Cat. 5, 100 meters max Gigabit Ethernet: 4-pair UTP Cat. 5, 5e, 6, 100 meters max |
| Data Rate | Ethernet: 10Mbps/20Mbps (Half/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full-Duplex) Gigabit Ethernet: 2000Mbps (Full-Duplex) |
| Protocol | CSMA/CD |
| Topology | Star |
| Interface | 8 10/100/1000Mbps Auto-MDIX RJ-45 Ports |
| Data RAM Buffer | 144Kbyte per device |
| Filtering Table | 8K entries per device |
| Power Consumption | 7.5 watts (max) |
| Diagnostic LED | Power, Link/ACT, 100Mbps, 1000Mbps |
| Power Adapter | 7.5V DC, 1A External Power Adapter |
| Dimension | 171 x 98 x 28mm (6.7 x 3.86 x 1.1 inches) |
| Weight | 450g (15.9oz.) |
| Temperature | Operating: 0° ~ 40° C (32° ~ 104° F) Storage: -10° ~ 70° C (14° ~ 158° F) |
| Humidity | Operating: 10%~90% (Non-Condensing) Storage: 5%~90% (Non-Condensing) |
| Safety Emissions | FCC, CE |

Package Contents						Related Products

- TEG-S80TXE							- TEG-S50TXE

- Multi-Language Quick Installation Guide			- TEG-PCBUSR

- TEG-PCITXR

To order please call: 888-326-6061 •  Sales: sales@trendnet.com

Support: support@trendnet.com • Technical Support: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

Back View

8-Port 10/100/1000Mbps Gigabit Switch

TEG-S80TXE Gigabit Ethernet Switch consists of eight 10/100/1000Mbps Gigabit Ethernet ports with Auto-negotiation and Auto-MDIX features. Users can connect Server(s) to the Gigabit port(s) to increase network performance or cascade Gigabit Switches together to create high-bandwidth Gigabit backbones. The TEG-S80TXE provides simple migration, scalability and flexibility to handle new applications and data types making it a highly reliable and cost effective solution for high-speed network connectivity.

#### TEG-S80TXE (C1.0R)

Network Solution for TEG-S80TXE

New Implement:

- New Housing

- New Chipset

Port Interface