FEATURES

- Uses 2.4 GHz frequency band, which complies with worldwide requirements

- 32-Bit PCMCIA CardBus Type II interface; supports Hot Swap and Plug & Play

- Up to 54Mbps connection speed

- Connects to IEEE 802.11g or 802.11b (11Mbps) wireless devices

- Dynamically shifts network speed (based on signal strength)

- Build in diversity antenna with LEDs indicating link status

- Supports Ad-Hoc (peer-to-peer) mode and Infrastructure mode (Access Point)

- Compatible with Windows 98SE/ME/2000/XP

- 64/128-bit Wired Equivalent Privacy (WEP) with ASCII, HEX, or Passphrase Key

- Stores multiple Wireless Network Profiles

- Low interference and high susceptibility guarantee reliable performance

- Low power consumption and easy configurations

- Enables high data rate multi-media applications such as video streaming transmission

- Distance coverage 30 to100 meters indoor, 100 to 300 meters outdoors

- 3-year Warranty

TREND SPEC’S

Adapter Type:	32-bit CardBus PCMCIA Type II (fits PCMCIA Type II or Type III slot)

Standards:	IEEE 802.11g draft and IEEE 802.11b

Driver Supports:	Windows 98SE/ME/2000/XP

Data Rate (auto fallback):	802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps

802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps

Module Technique:	802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps)

802.11g: OFDM

Antenna:	Build-in Diversity Patch Antenna

Media Access Protocol:	CSMA/CA with ACK

LED Indicator:	Power, Link

Frequency:	2.4 to 2.497GHz (Industrial Scientific Medical Band)

Output Power:	15dBm (max.)

Receiving Sensitivity:	11Mbps 10 – 5 BER @ -80 dBm (typical)

54Mbps 10 – 5 BER @ -65 dBm (typical)

Power Consumption:	Operating: 3.3VDC (TX: 550mA, RX: 350mA). Idle: 3.3VDC, 225mA.

Radio Disabled: 3.3VDC <10mA

Channels:	11 Channels (US/Canada), 13 Channels (EU)

Dimensions (L x W x H):	118 x 54 x 8.5 mm (4.65 x 2.1 x 0.33 inches)

Weight:	42.5g. (1.5 oz.)

Operating Temperature:	0( ~ 50( C (32( ~ 122( F)

Storage Temperature:	-20( ~ 65( C (-4( ~ 149( F)

Humidity:	Max. 95% (Non-condensing)

Certification:	FCC, CE

TOP REASONS THE TEW-401PC IS A LASTING TREND

Economical:	Save time, labor, and materials; compare with wired network installation.

Flexible:	Creates wireless peer-to-peer network in Ad-Hoc mode or connects to Ethernet LAN in Infrastructure mode using Wireless Access Point or Wireless Router.

Cost Effective:	Supports IEEE 802.11b and IEEE 802.11g draft standards; connects to any IEEE 802.11b and 802.11g wireless network.

Performance:		54Mbps high-speed wireless connection.

TEW-401PC	54Mbps 802.11g Wireless PC Card

TEW-403PI	54Mbps 802.11g Wireless PCI Network Adapter

TEW-410APB	54Mbps 802.11g Wireless Access Point + Bridge + Repeater

TEW-411BRP	54Mbps 802.11g Wireless Broadband Router + Access Point + Bridge

TEW-PS3	3-Port (Parallel) 802.11b Wireless Ethernet Print Server

TEW-PS1U	11Mbps Wireless USB port Multi-Protocol Print Server

# To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com 	ss06222003

# Text boxes

54Mbps 802.11g Wireless PC Card

TRENDnet's TEW-401PC 54Mbps Wireless CardBus PC Card is the latest creation for Notebook computer’s wireless network applications. It complies with IEEE 802.11g draft and PCMCIA CardBus standards, operating with 2.4GHz Direct Sequence Spread Spectrum (DSSS) transmission technology, and compatible with 802.11b 11Mbps wireless devices. With the wireless networking products, users can setup Local Area Network (LAN) without the trouble of installing networking cables.

TEW-401PC

IEEE 802.11b/11g Wireless Network Solution

Product Information