FEATURES

- Uses 2.4 GHz frequency band (DSSS), which complies with worldwide requirements

- Supports IEEE 802.11g or 802.11b (11Mbps) wireless devices

- Dynamic data rate shift at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic data rate shift at 11, 5.5, 2 and 1Mbps for 802.11b

- Supports Ad-Hoc (peer-to-peer) mode and Infrastructure mode (Access Point)

- Compatible with Windows 98(SE)/ME/2000/XP

- Supports 64/128-bit Wired Equivalent Privacy (WEP)

- Supports Wireless Fidelity Protected Access (WPA)

- Low interference and High susceptibility guarantee reliable performance

- 2dBi Detachable antenna with female Reverse SMA connector

- Distance Coverage 35~100 meters indoor, 100~300 meters outdoor (depending on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

TREND SPEC’S

Interface Type:		32-bit PCI 2.1, 2.2 Bus Master

Standards:		IEEE 802.11b and IEEE 802.11g

Antenna:		2dBi Detachable Antenna (Female Reverse SMA Connector)

Data Rate (auto fallback):		802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps

802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps

Module Technique:			802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps)

802.11g: OFDM

Media Access Protocol:		CSMA/CA with ACK

Frequency:		2.4 to 2.497 GHz (Industrial Scientific Medical Band)

LED Indicator:		Link

Antenna:		1 x 2dBi Detachable Dipole Antenna with Female Reverse SMA Connector

Output Power:		15dBm (typical) @ 802.11b

12dBm (typical) @ 802.11g

Receiving Sensitivity:		54Mbps 10 – 5 BER @ -73 dBm (typical)

22Mbps 10 – 5 BER @ -85 dBm (typical)

11Mbps 10 – 5 BER @ -86 dBm (typical)

Encryption:			64/128-bit

Support OS:			Windows 98(SE), ME, 2000, XP

Channels:		       1~11 channels (FCC), 1~13 channels (ETSI), 1~14 channels (MKK-Japan),

10~13 channels (France), 3~9 channels (Israel)

Power Consumption:		Receive Mode: 480mA

Transmit Mode: 650 mA

Dimensions (LxWxH):		 133 x 121 x 21.6 mm (5.2  x 4.8 x 0.85 inches) (without metal bracket)

Weight:		 63.5 g ( 2.2 oz.) (with antenna)

Operating Temperature:			0( ~ 40( C (32( ~ 104( F)

Storage Temperature:			-20( ~ 70( C (-4( ~ 158( F)

Humidity:			10% ~ 95% max. (Non-condensing)

Certification:			FCC, CE, ETS

##### TOP REASONS THE TEW-423PI IS A LASTING TREND

Economical:	Save time, labor, and materials; compare with wired network installation.

Flexible:	Creates wireless peer-to-peer network in Ad-Hoc mode or connects to Ethernet LAN in Infrastructure mode using Wireless Access Point or Wireless Router.

Cost Effective:	Supports IEEE 802.11b and IEEE 802.11g standards; connects to any IEEE 802.11b and 802.11g wireless network.

Performance:	54Mbps high-speed wireless connection.

TEW-423PI	802.11g 54Mbps Wireless PCI Adapter

TEW-421PC	802.11g 54Mbps Wireless PC Card

TEW-431BRP	802.11g 54Mbps Wireless Router

TEW-410APB	54Mbps Wireless Access Point + Bridget

TEW-IA04O	4dBi Indoor Omni Antenna

TEW-IA06D	6dBi Indoor Directional Antenna

TEW-OA14DK	14dBi OutdoorDirectional Antenna

TEW-OA24D	24dBi Outdoor Directional Parabolic Antenna

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

### 54Mbps 802.11g Wireless PCI Adapter

TRENDnet's TEW-423PI 54Mbps Wireless PCI Card cuts the wires to your desktop and provides 54Mbps speed to handle bandwidth-intensive applications. It complies with the IEEE 802.11g standard, making it backward compatible with 802.11b networks for assured compatibility. Advanced Wi-Fi Protected Access (WPA) and up to 256-bit WEP encryption are supported to provide secure access for your data. Cut the wires and move your desktop where you need it with TRENDnet’s 802.11g wireless PCI Card.

#### TEW-423PI

Product Information

IEEE 802.11g Wireless Network Solution