Features

- Wi-Fi Compliant with IEEE 802.11g and 802.11b Wireless Standards

- Uses 2.4 GHz Frequency Band, which Complies with Worldwide Requirements

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure (AP-Client) Mode

- Compliant with Universal Serial Bus Rev 2.0, 1.1, 1.0 Specifications

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Compatible with Windows 98SE/ME/2000/XP

- Supports 64/128-bit WEP, WPA/WPA2 and WPA-PSK/WPA2-PSK

- Support WMM™ QoS (Wi-Fi Multimedia Quality of Service)

- Integrated Printed Antenna for the Multi-Path Environment

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Low Power Consumption and Easy Configurations

- Range of 35~100 meters indoor, 100~300 meters outdoor (depends on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | USB 2.0, 1.1, 1.0 Compliant |
| Standards | IEEE 802.11b and IEEE 802.11g |
| Antenna | 2dBi Integrated Printed Antenna |
| LED Indicator | Link |
| Power Consumption | Receive Mode: 280mA Transmit Mode: 380 mA |
| Supported OS | Windows 98(SE), ME, 2000, XP(SP1/SP2) |
| Dimensions (LxWxH) | 80 x 30 x 12 mm (3.1 x 1.2 x 0.5 inches) |
| Weight | 15 g (0.5 oz.) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104( F) Storage: -10( ~ 70( C (14( ~ 158( F) |
| Humidity | 10% ~ 95% max (Non-condensing) |
| Certification | FCC, CE, ETS |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM |
| Frequency | 2.412 to 2.484 GHz (Industrial Scientific Medical Band) |
| Media Access Protocol | CSMA/CA with ACK |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps **6Mbps for 802.11g using USB 1.1 or 1.0 Connection |
| Output Power | 15dBm (typically) @ 802.11b 12dBm (typically) @ 802.11g |
| Receiving Sensitivity | 54Mbps 10% PER @ -72 dBm (typical) 11Mbps 8% PER @ -83 dBm (typical) |
| Security | 64/128-bit WEP (Hex/ASCII), WPA/WPA2, WPA-PSK/WPA2-PSK |
| Channels | 1~13 Channels (Universal Domain Support) |

Package Contents					Related Products

- TEW-424UB 					- TEW-421PC

- Quick Installation Guide				- TEW-423PI

- Utility & Driver CD-ROM				- TEW-431BRP

- 1 x USB 2.0 Cable (145mm/5.7inches)

# To order please call: 1-888-326-6061 (USA)

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hotline: (866)845-3673

## www.TRENDNET.com

# Text boxes

54Mbps 802.11g Wireless USB 2.0 Adapter

TEW-424UB 802.11g Wireless USB 2.0 Adapter brings together the convenience of USB 2.0 and the high speed of 802.11g, allowing you to easily connect to 802.11g networks at speeds of up to 54Mbps. The USB 2.0 interface facilitates a hassle-free Plug-and-Play installation, and 128-bit WEP Encryption provides robust network security. The TEW-424UB is a feature-rich yet convenient way to go wireless.

New Implements

- New Compact Housing

- 1~13 Universal Domain Support

- WMM™ QoS support

TEW-424UB (V2.1R)