Features

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Wireless Devices

- Supports Router (Router+Modem) or Modem (Modem only) Mode

- Compliant with ADSL, ADSL2, ADSL2+ on G.dmt, G.lite and T1.413 Multi-Mode PSTN Environments

- Compliant with PPPoE, PPPoA or IPoA Connection Types

- Provides 64/128-bit Wired Equivalent Privacy (WEP) and WPA-PSK Encryption

- Supports Filtering by URL, MAC Address, Services and Date/Time

- Supports Virtual DMZ, Virtual Servers (Port Forwarding) and Firewall Rules

- Supports RIP/Static Routing and Dynamic DNS Service

- Supports up to 100 VPN Pass-Through sessions for PPTP, IPSec or L2TP connections

- NAT/NAPT, Rule-Based and SPI Firewall protect against DoS (Denial of Service) attacks

- Real-Time email alert and logs when attack/unauthorized Internet activity occurs

- DHCP Server feature supports up to 253 Users

- Supports UPnP (Universal Plug & Play) and ALGs Support Internet applications such as Email, FTP, Gaming, ICQ,

Net Meeting, PING, Telnet, and more

- Supports most operating systems, such as Windows 95/98/ME/NT/2000/XP, Unix, and Mac

- Easy Configuration and Remote Management with Web Browser (HTTP)

- Supports SSID Enable/Disable Broadcasting Feature

- Built-in Flash memory for firmware upgrade

- Range of 35~100 meters indoor, 100~300 meters outdoor (depending on the environment)

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T; IEEE 802.3u 100Base-TX; IEEE 802.11g, IEEE 802.11b |
| Protocols | NAT/NAPT, PPPoE&PPPoA, HTTP, DHCP(Client/Server), TVP/IP & UDP, PAP & CHAP, RIP1, RIP2, DDNS, UPnP |
| Firewall | NAT Firewall with ALGs, Rule-Based Policy Firewall, DoS (Denial of Service) attack Firewall; E-mail Alerts and Log |
| Security | URL Filter, Access Control, Local Password |
| VPN Pass Through | PPTP, IPSec, L2TP (up to 100 sessions) |
| VPN IPSec Client | Up to 8 Simultaneous IPSec Tunnels Throughput 1.5Mbps |
| ATM | TM Cell over AAL5 Support UBR/CBR/VBR VPI Range (0-255) and VCI range (32-65535) Support 4PVCs Support OAM F4/F5 loop back Payload Encapsulation RFC2684 (RFC 1483 / 2684), multi-protocol over ATM RFC2684 (RFC 1483 / 2684), Bridge mode RFC2225 (RFC 1577), IPoA RFC2364, PPP over ATM (CHAP and PAP supported) RFC2516, PPPoE (PPP over Ethernet) over ATM Support auto-detection for VPI/CVI and multiplexing method (VC-based, LLC-based) |
| Management | Web-Based Management (HTTP) |
| WAN Port (ADSL line Interface) | Complies with G.dmt (G.992.1) Annex A Complies with G.lite (G.992.2) and T1.413 Annex A ITU G.992.3 Annex A ADSL2, ITU G.992.5 Annex A ADSL2+ RJ-11 connector, Line Impedance: 100 Ω |
| LAN Port | 4 x 10/100Mbps Auto-MDIX and Auto-Negotiation RJ-45 Port |
| Reset Button | Reset to Factory Default |
| LED | Power, Status, 4x100LAN, 4x10LAN, ADSL, WLAN, Internet |
| Power | 12V DC 1A External Power Adapter |
| Dimensions | 175 x 115 x 30mm (6.9 x 4.5 x 1.2 inches) |
| Weight | 280g (9.9 oz) |
| Temperature | Operating: 0˚~ 40˚C (32˚~ 104˚F) Storage: -20˚~ 70˚C (-4˚~ 158˚F) |
| Humidity | Operating: 10 ~ 90% RH Storage: 5 ~ 95% RH |
| Emissions | FCC, CE |
| Wireless |
| Standards | IEEE 802.11b, IEEE 802.11g |
| Modulation | 802.11b: DSSS (PBCC, CCK, DQPSK, DBPSK) 802.11g: OFDM |
| Data Rate (Auto Fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps |
| Frequency Range | 2.4 ~ 2.497 GHz |
| Channel | 1~14 Channel (Universal Domain Selection) |
| Antenna | 1 x 2dBi External Detachable Dipole Antenna with Reverse SMA Connector |
| Security | 64/128-Bit WEP (Hex or Passphrase), WPA-PSK (TKIP) |
| Output Power | 802.11b: 18dbm 802.11g: 12 ~ 14dbm |
| Receiving Sensitivity | 11Mbps 10 – 5 BER @ -82 dBm (typical) 54Mbps 10 – 5 BER @ -72 dBm (typical) |

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Tech Support Hotline: (866)845-3673

Sales: sales@trendnet.com • Support: support@trendnet.com

www.TRENDNET.com

# Text boxes

New Implements

- New Standing Style Housing

- RoHS Compliant Hardware

- Chipset  ( Marvell88E6060

Package Contents

- TEW-435BRM

- Quick Installation Guide

- CD-ROM (User’s Guide)

- 1 x 1.5m (5ft.) Cat.5 Cable

- 1 x RJ11 Telephone Cable

- Power Adapter (12V DC 1A)

Related Products

- TEW-421PC

- TEW-423PI

- TW100-BRM504

54Mbps 802.11g ADSL Firewall Modem Router

TEW-435BRM delivers the most complete high-performance network solution. It includes a Wireless 802.11g 54Mbps Access Point, ADSL Modem, Firewall, Internet Router, and 4-Port Switch. The TEW-435BRM offers all-in-one Internet and network access. Advanced security includes Stateful Packet Inspection (SPI) Firewall and Application Level Gateway (ALG) for secured online communications.

TEW-435BRM (C1.0R)