Features

- Wi-Fi Compliant with IEEE 802.11a, 802.11g and IEEE 802.11b Standards

- Uses 5 GHz or 2.4 GHz Dual Band Design, which Complies with Worldwide Requirements

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure (AP-Client) Mode

- Supports Super AG technology Data Rate up to 108Mbps

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11a/g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Compatible with Windows 2000/XP (SP1/SP2)/2003 Server

- Supports 64/128-bit WEP, WPA (AES/TKIP) without Performance Degradation

- Supports Wireless Multimedia Enhancements Quality of Service (Qos)

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Range of up to 100 meters indoors, 250 meters outdoors (depends on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | 32-Bit PCI Rev. 2.1/2.2 |
| Standards | IEEE 802.11a, IEEE802.11b and IEEE 802.11g |
| Power Consumption | Receive Mode: 280mA(max) ; Transmit Mode: 510 mA(max) |
| Supported OS | Windows 2000/XP(SP1/SP2), 2003 Server |
| Dimensions (LxWxH) | 120 x 40 x 4 mm (4.72 x 1.57 x 0.16 inches) (without metal bracket) |
| Weight | 63.5 g (2.2 oz.) (with antenna) |
| Temperature | Operating: 0( ~ 50( C (32( ~ 122( F) Storage: -25( ~ 70( C (-13( ~ 158( F) |
| Humidity | 10% ~ 90%max (Non-condensing) |
| Certification | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11a/g: OFDM with BPSK, QPSK and 16/64-QAM Sub-Carrier Modulations |
| Antenna | (1dBi 11g, 2dBi 11a) Dual Band Detachable Antenna (Female Reverse SMA Connector) |
| Frequency | 802.11a: UNII-Band 5.15 ~ 5.825 GHz 802.11b/g: ISM-Band 2.400 ~ 2.484GHz |
| Media Access Protocol | CSMA/CA |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11a/g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps Super AG: 108Mbps |
| Transmit Power | 802.11a: 15dBm (typical) 802.11b: 18dBm (typical) 802.11g: 16dBm (typical) |
| Receiving Sensitivity | 802.11a: 54Mbps 10 – 5 BER @ -68 dBm (typical) 802.11b: 11Mbps 10 – 5 BER @ -88 ±2 dBm (typical) 802.11g: 54Mbps 10 – 5 BER @ -68 dBm (typical) |
| Encryption | 64/128-bit WEP, WPA |
| Channels | 11a: Subject to Local Regulations 11b/g: 1~11 (US), 1~13 (EU) |

##### TOP REASONS THE TEW-503PI IS A LASTING TREND

| Economical | Save Time, Labor, and Materials; Compare with Wired Network Installation |
| --- | --- |
| Flexible | Creates wireless peer-to-peer network in Ad-Hoc mode or connects to Ethernet LAN in Infrastructure mode using Wireless Access Point or Wireless Router |
| Cost Effective | Supports IEEE 802.11a, IEEE 802.11b and IEEE 802.11g Standards; Connects to any IEEE 802.11a and 802.11b/g wireless network |
| Performance | 108Mbps High Speed Wireless Connection |

Package Contents				Related Products

- TEW-503PI					- TEW-501PC

- Utility & Driver CD-ROM			- TEW-504UB

- Multi-Language Quick Installation Guide	- TEW-510APB

- TEW-511BRP

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

Official Site: www.TRENDNET.com

# Text boxes

### TEW-503PI

### 108Mbps 802.11a/g Wireless PCI Adapter

TRENDnet's TEW-503PI 802.11a/g Wireless PCI adapter is a versatile network that connects your workstation to 802.11a, 802.11b, or 802.11g wireless networks.  You can experience blazing download speeds at up to 108Mbps.  The TEW-503PI also provides advanced wireless security features such as WPA with TKIP and AES encryption algorithms.

Wireless Network Solution for TEW-503PI

*Due to European Wireless Regulations, Super A mode is not supported in the EU version